## Slide 1: Embedded supercomputing
For hobbyists
Prashant Sohani (08007017) <prashant.sohani@iitb.ac.in>
<psohani@nvidia.com>

## Slide 2: What is computation?
A very broad description:
  A mapping of abstract ideas into physical objects
    Eg: Electrons/fields can represent numbers
  A system of physical objects whose natural behaviour resembles abstract operations
    Eg: A binary adder is purely driven by the laws of electrodynamics, and yet the result is similar to what we call ‘addition’
Why such a broad description?
  Babbage’s Analytical Engine is also a computer!
  And yet, plenty of assumptions:
    linearity/causality of time,
    invariance of physical laws (spatially, temporally local)

## Slide 3
The Babbage Engine
[ http://www.computerhistory.org/babbage/ ]
The past..
“Another age must be the judge”
“[The Babbage Engine is] … the wonder of a future already passed.”
- Computer History Museum

## Slide 4
Tianhe-2
[http://www.top500.org/featured/systems/tianhe-2/ ]
D-Wave Two
[http://www.nas.nasa.gov/quantum/quantumcomp.html ]
The present

## Slide 5
“Parallel Quantum Computation” - Norman Margolus
MIT Laboratory For Computer Science, June 1989
This slide inevitably left (almost) blank
The future..

## Slide 6: Side note: Fredkin gate
Universal gate!
‘Reversible computation’
Thermodynamic implications:
  Most energy-efficient at transforming information
The top control input goes through unchanged (A’ = A), and the bottom inputs either go straight through also (if A = 1) or cross (if A = 0 then B’ = C and C’ = B)
“Parallel Quantum Computation” - Norman Margolus; MIT Laboratory For Computer Science, June 1989
http://en.wikipedia.org/wiki/Fredkin_gate

## Slide 7: Important questions
What is the ‘nature’ of the ever-increasing computational power?
Where and how to use this power optimally?
Why should a hobbyist care?

## Slide 8: Important questions (contd.)
Where and how to use this power?
  Along (at least) 3 separate dimensions:
Why should a hobbyist care?
  Casual: More computational power is good
  Competitive: More computational power is good!
Peripheral count
Per-peripheral complexity
Algorithmic complexity

## Slide 9
[ http://www.gotw.ca/publications/concurrency-ddj.htm ]
The Free Lunch Is Over:
A Fundamental Turn Toward Concurrency in Software

## Slide 10: Single vs multi-threaded line-follower
Single-threaded:
  “First read sensors, then do math, then drive motors”
Multi-threaded:
  “Keep reading sensors”
  “And also keep doing math”
  “And also keep driving motors”
  “And also keep flashing decorative LEDs”
  “And also keep playing some background music”
  …
  “And also control the universe, while you’re at it!”

## Slide 11: Why multi-threading?
May seem more complex to manage:
  Need to synchronize; load-balance the threads,
  Need to move data without ‘race conditions’, etc.
But has benefits too:
  Flexible
    Scalable to multi-core processors
  Performant
    Related operations grouped together => better optimization
  Modular
    A single slow/faulty thread need not halt the system:
      “If the music stops, the line-follower doesn’t have to!”

## Slide 12: Single-core single-threading
Single-threaded application:
  Execute only one task at a time
  Can use HW interrupts to ‘simulate’ more tasks:
Code executing
Incoming interrupt!
Execute interrupt routine
Resume code execution

## Slide 13: Single-core ‘simulated’ multi-threading
Essentially a single-threaded application,
  with timer-based context-switching:
On small platforms, you may use your own context-switcher, like above
  ‘Context’: Register values, program counter etc.
  Protothreads: http://dunkels.com/adam/pt/
Thread 1 executing
Incoming timer interrupt!
Save thread 1 context; load thread 2 context
Schedule next timer interrupt
Start thread 2 execution

## Slide 14: Hardware-based multi-threading
Implementation: beyond the scope of this session
  Best left to OS-level thread scheduler, if available
  [ http://playground.arduino.cc/Code/OsWrap ]
Other things not covered here:
  Thread synchronization
    Eg. AV playback
    Wait for events/messages as a sync point
  [ http://playground.arduino.cc/Code/OsWrap#MessageQ ]
  Prevent race conditions on same data access
    Obtain ‘locks’ before read/write to shared data [http://playground.arduino.cc/Code/OsWrap#Semaphores ]

## Slide 15: Multi-threaded “Hello world!”
#include <iostream>
#include <string>
using namespace std;
int main(){
int pid;
string text[4]={“zero",“one",“two",“three"};
for (int i=0;i<4;i++){
pid=fork();
if (pid>0){
cout << "Thread " << text[i] << " says Hello World!" << endl;
exit(0);
}
}
return 0;
}

## Slide 16: Multi-threaded “Hello world!”
#include <iostream>
#include <string>
using namespace std;
int main(){
int pid;
string text[4]={“zero",“one",“two",“three"};
for (int i=0;i<4;i++){
pid=fork();
if (pid>0){
cout << "Thread " << text[i] << " says Hello World!" << endl;
exit(0);
}
}
return 0;
}
i= 0 1 2 3 4

## Slide 17: Multi-core CPUs
CPU cores: Ideal for a few, individual tasks
  Heavy-duty, ultra-low latency processing
What if.. we need to perform the same task many times, on different data sets?
  Theoretically, a CPU can operate on each data set, one at a time (or #cores at a time)
  Each CPU core is heavy-duty, so #cores is limited
  Time-to-finish: may be too much!

## Slide 18: GPUs for parallel computing
3D graphics rendering:
  Needs the same calculations for each vertex/pixel
  Has to be done fast (More frames-per-second!)
    More latency than CPUs, but more throughput also
GPUs initially had only 3D rendering functions; but now can do any parallel computing task:
  “GPGPU”: General-Purpose computing on GPUs

## Slide 19: CPU vs GPU comparison
Different specializations, for different tasks
CPUs for Serial processing:
A few high-power cores, that can perform various tasks
Low-latency low-throughput
Typical: 4 / 16 / 32,000 cores!
GPUs for Parallel processing:
Many low-power cores, that can
all simultaneously perform the same task
High-latency high-throughput
Typical: 192 / 2048 / 46 million cores!

## Slide 20: GPUs: Why should hobbyists care?
Most mobile devices have GPUs
Mobile GPUs: highest FLOPS/W on the planet.
[ Even more than supercomputers! ]
  Due to focused design on power-efficiency
Same GPUs available on embedded platforms
Easy to program C/C++ with CUDA, OpenCL

## Slide 21: CUDA “Hello World!”
#include "stdio.h“
__global__ void add(int *a, int *b, int *c){
c[threadIdx.x] = a[threadIdx.x] + b[threadIdx.x];
}
int main(){
int a={1,2,3,4};
int b={5,6,7,8};
int c[4];
int *dev_c;
cudaMalloc((void**)&dev_c, 4*sizeof(int));
add<<<1,1>>>(a,b,dev_c);
cudaMemcpy(&c, dev_c, 4*sizeof(int), cudaMemcpyDeviceToHost);
for(int i=0;i<4;i++){
printf("%d + %d is %d; Hello World!\n", a[i], b[i], c[i]);
}
cudaFree(dev_c);
return 0;
}

## Slide 22: CUDA “Hello World!”
#include "stdio.h“
__global__ void add(int *a, int *b, int *c){
c[threadIdx.x] = a[threadIdx.x] + b[threadIdx.x];
}
int main(){
int a={1,2,3,4};
int b={5,6,7,8};
int c[4];
int *dev_c;
cudaMalloc((void**)&dev_c, 4*sizeof(int));
add<<<1,4>>>(a,b,dev_c);
cudaMemcpy(&c, dev_c, 4*sizeof(int), cudaMemcpyDeviceToHost);
for(int i=0;i<4;i++){
printf("%d + %d is %d; Hello World!\n", a[i], b[i], c[i]);
}
cudaFree(dev_c);
return 0;
}

## Slide 23: FPGAs
Field-Programmable Gate Arrays:
  ‘LEGO’ kit to build your own processor
Used to contain only primitive logic blocks (AND-OR, Flip-flop arrays)..
  Can be used to implement fixed-point arithmetic
..but modern FPGAs have higher-level blocks:
  Floating Point Units (FPUs)
  Signal processing blocks (DSPs)

## Slide 24: FPGAs vs processors
Advantages:
  Customizable:
    Logic paths, ’macro-blocks’ can be greatly fine-tuned for specific algorithms
  Parallel:
    Each logic block can do some useful work in every clock cycle
  Reconfigurable:
    Can ‘reprogram’ the chip again and again
Disadvantages:
  Need to use Hardware Description Language (VHDL)
    Essentially, you are a microprocessor architect!
  Could be harder to migrate from one architecture to another
Similar, low complexity solution: CPLDs

## Slide 25: Examples of platforms: Multi-core CPU boards
Samsung Arndale board [ http://www.arndaleboard.org ]
  Arndale Octa board
    8 cores @ 1.8GHz/1.2GHz; big.LITTLE configuration
    70 FP32 GFLOPS
    $199
Adapteva Parallella Boards [ http://www.adapteva.com/ ]
  Parallella 16 Micro-server
    ARM Dual-core + Epiphany 16-core @ 1GHz
    32 GFLOPS
    $99

## Slide 26: Examples of platforms: FPGA boards
Xilinx FPGA boards
  Elbert V2 Spartan 3A board
    ~1500 logic cells
    $39
Altera FPGA Boards
  Cyclone Altera EP1C3T144 board
    ~3000 logic cells
    $39

## Slide 27: Examples of platforms: GPU boards
NVIDIA Jetson TK1 [https://developer.nvidia.com/jetson-tk1 ]
  Quad CPU cores (+ 1 power-saver core)
  192 GPU cores!
    300 GFLOPS
    $199

## Slide 28: The hierarchical building blocks of a modern computing device
Maxwell’s equations | The silicon atom | P-N Junction
Digital circuits | Logic gates | Transistors
The microprocessor | Software code | User application

## Slide 29: Applications
104 parallel computing project ideas:
  http://www.adapteva.com/white-papers/104-parallel-computing-projects-for-next-summer/
Basically, anything a human can do

## Slide 30: Robotics
Needs multithreading, to:
  collect data from multiple sensors;
  control multiple actuators
Suitable platforms:
  Multi-core CPUs for control-centric devices
    Robotic arms; Biped bots
  FPGAs for a more dynamic complexity control:
    If you need signal processing before control logic

## Slide 31: Machine learning
Let machines ‘learn’, similar to how we learn
Usually follows ‘train  guess  correct’ loop
Supervised learning vs unsupervised learning
Model
Training Data
Guess
Eval
Feedback
[Optional] Expected response

## Slide 32: Artificial Neural networks
A general model, similar to biological ones:
  Hierarchical classification of data/signals
  Various types: Convolutional/deep neural nets
Important Landmark:
  ANN image recognition has surpassed human-level accuracy in February 2015!!
  This is still narrow AI; cannot do ‘everything’

## Slide 33: Model of an artificial neuron
Weighted sum of inputs  non-linear function
Popular non-linear function choices:
  Piece-wise linear; step function, sigmoids etc.
…
…

## Slide 34: Deep neural networks
Input
Output

## Slide 35: Applications of ML:
Machine learning for..
  Natural language processing
  Speech recognition
  Object/feature detection (Line follower on steroids!)
Weights training:
    can be offline;
    decoupled from weights usage
Suitable platforms for training:
  More the parallelism; faster the training
  GPU ‘farms’ are ideal; but even 1 GPU is better than none
For weights application:
  Different platforms, depending upon model complexity

## Slide 36: Computer vision
Example: Automated toll system
Requirements:
  Image processing (OpenCV-like capabilities)
  Encryption layer, for security reasons?
Suitable platforms:
  High-end FPGAs (need DSP blocks)
  Embedded GPU boards
    Can use GPU-accelerated libraries

## Slide 37: Putting it all together
Sensor inputs; image processing (OpenCV)
Navigation/collision avoidance (ML)
Actuators (Robotics)
=

## Slide 38: Thank you!
Questions?