RCBus Specification

Version 0.0.002
24-February-2023

Introduction	3

Backplanes and Modules	4

Bus Connectors	5

Bus Pin Assignments	6

Bus Signals	8

Guidance for Designers	10

Unresolved Issues & Notes	11

Appendix A - Background	12

Appendix B - RC2014TM USER Pin Usage	14

Appendix C - Bus Conventions For Mapping Motorola Busses	16

Introduction	16

Mapping The Bus	16

Mapping The Extended Bus	16

Additional Signals	17

Notes	17

## Introduction

The documentation describes the Retro Computer Bus (RCBus).

The RCBus is an extended version of the RC2014TM bus.

The RCBus has been created for the following reasons:

- To help distinguish RC2014TM products from products that are not RC2014TM but that claim a degree of compatibility with RC2014TM

- To reduce the chances of trademark infringement

- To help members of the retro computer community share designs and sell products based on the RC2014TM bus

- To specify a common approach to supporting features not provided by the RC2014TM bus

- To specify a common approach to supporting processors other than the Z80

Appended A provides some background information which should help explain the above list of reasons for creating the RCBus.

The RCBus has a common backplane but some of the signals are not required for some use cases and some signals have different functions depending on the processor and other factors. Modules connected to the backplane can either work with all other RCBus modules or, more likely, a sub-set of RCBus modules.

To indicate which modules are compatible with each other, a number of sub-specifications are documented, such as:

- RCBus-2014		This is the RC2014TM specification (see www.rc2014.co.uk)

  - RCBus-2014-s	RC2014TM standard (40-pin) bus

  - RCBus-2014-e	RC2014TM enhanced (>40-pin) bus

- RCBus-Z80		Includes extensions to support advanced Z80 family features

- RCBus-6800		Includes extensions to support the Motorola 6800 style processors

A module that only requires the RC2014TM standard 40-pin bus might be compatible with RC2014-2014-s, RCBus-2014-e, and RCBus-Z80. Of course, such a compatibility claim does not mean you can put any two “compatible” modules together and expect them to work. For example, two RC2014TM serial modules will not work due to address conflicts. What “compatible” means is the physical and electrical bus signals are compatible.

The term RCBus can be used for any design that works with the full RCBus backplane or a sub-set of the RCBus backplane.

## Backplanes and Modules

Below is an example of an RCBus module which has a partial second row of bus pins.

TODO backplanes

TODO: check connector dimensions

## Bus Connectors

The bus connectors are low cost header pins and sockets, either single or double row with up to 40-pins in each row.

Pin length ~6mm, pitch 2.54mm

Note that the most commonly used male 1x40 angled connector has a different profile to the 2x40 connector.

Single row bus socket viewed from above:

Pin 1

Pin 40

Front										Back

Double row bus socket viewed from above:

Pin 1										Pin 40

Pin 41										Pin 80

Front										Back

## Bus Pin Assignments

| Pin 1st row | RC2014TM standard | RCBus backplane | RCBus Z80 | RCBus 68xx | RCBus 9995 | Notional 16-bit CPU |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | A15 |  |  |
| 2 | A14 |  |  |
| 3 | A13 |  |  |
| 4 | A12 |  |  |
| 5 | A11 |  |  |
| 6 | A10 |  |  |
| 7 | A9 |  |  |
| 8 | A8 |  |  |
| 9 | A7 |  |  |
| 10 | A6 |  |  |
| 11 | A5 |  |  |
| 12 | A4 |  |  |
| 13 | A3 |  |  |
| 14 | A2 |  |  |
| 15 | A1 |  |  |
| 16 | A0 |  |  |
| 17 | GND |  |  |
| 18 | +5V |  |  |
| 19 | M1 |  |  |
| 20 | RESET |  |  |
| 21 | CLOCK |  |  |
| 22 | INT |  |  |
| 23 | MREQ |  |  |
| 24 | WR |  |  |
| 25 | RD |  |  |
| 26 | IORQ |  |  |
| 27 | D0 |  |  |
| 28 | D1 |  |  |
| 29 | D2 |  |  |
| 30 | D3 |  |  |
| 31 | D4 |  |  |
| 32 | D5 |  |  |
| 33 | D6 |  |  |
| 34 | D7 |  |  |
| 35 | TX |  |  |
| 36 | RX |  |  |
|  | 2014 | Backplane | Z80 | 68xx | 9995 | 16-bit |  |  |
| 37 | USER1 | n37 | INT1 | FIRQ | MEMEN | n37 |  |  |
| 38 | USER2 | n38 1 | IEI | E | CRUIN | n38 1 |  |  |
| 39 | USER3 | n39 1 | IEO | RW | CRUCLK | n39 1 |  |  |
| 40 | USER4 | n40 | n40 | n40 | n40 | n40 |  |  |

1  Backplane configurable for direct or cascade (daisy-chain) connections

| Pin 2nd row | RC2014TM enhanced | RCBus Backplane | RCBus Z80 | RCBus 68xx | RCBus 9995 | Notional 16-bit CPU |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 41 | N/A | 3v3 |  |  |
| 42 | N/A | n42 1 | BAI | n42 | n42 | n42 |  |  |
| 43 | N/A | n43 1 | BAO | n43 | n43 | n43 |  |  |
| 44 | N/A | n44 ? USER# | n44 | n44 | n44 | n44 |  |  |
| 45 | N/A | n45 ? HiLo byte | n45 | n45 | n45 | n45 |  |  |
| 46 | N/A | n46 | n46 | n46 | n46 | n46 |  |  |
| 47 | N/A | n47 | n47 | n47 | n47 | n47 |  |  |
| 48 | N/A | n48 | n48 | n48 | n48 | n48 |  |  |
| 49 | N/A | A23 |  |  |
| 50 | N/A | A22 |  |  |
| 51 | N/A | A21 |  |  |
| 52 | N/A | A20 |  |  |
| 53 | N/A | A19 |  |  |
| 54 | N/A | A18 |  |  |
| 55 | N/A | A17 |  |  |
| 56 | N/A | A16 |  |  |
| 57 | GND |  |  |
| 58 | +5V |  |  |
| 59 | RFSH |  |  |
| 60 | PAGE |  |  |
| 61 | CLOCK2 |  |  |
| 62 | BUSACK |  |  |
| 63 | HALT |  |  |
| 64 | BUSRQ |  |  |
| 65 | WAIT |  |  |
| 66 | NMI |  |  |
| 67 | D8 |  |  |
| 68 | D9 |  |  |
| 69 | D10 |  |  |
| 70 | D11 |  |  |
| 71 | D12 |  |  |
| 72 | D13 |  |  |
| 73 | D14 |  |  |
| 74 | D15 |  |  |
| 75 | TX2 |  |  |
| 76 | RX2 |  |  |
|  | 2014 | Backplane | Z80 | 68xx | 9995 | 16-bit |  |  |
| 77 | USER5 | n77 | INT2 | n77 | n77 | n77 |  |  |
| 78 | USER6 | n78 | n78 | n78 | n78 | n78 |  |  |
| 79 | USER7 | n79 | n79 | n79 | n79 | n79 |  |  |
| 80 | USER8 | n80 | n80 | n80 | n80 | n80 |  |  |

1  Backplane configurable for direct or cascade (daisy-chain) connections

## Bus Signals

This section describes each of the common signals. Details of bus signals with multiple uses (those labelled n##) can be found in the appropriate appendix.

Singals are TTL level unless otherwise indicated. It is recommended that CMOS ICs be used wherever possible and that 74HCT series ICs are used rather than of 74 series families.

Signals are defined by their function with a Z80 CPU unless otherwise stated.

+5V	VPower supply +5 volts, recommended tolerance +/-0.25 volts.

+3V3	Power supply +3.3 volts. Optional.

A0 to A23	Processor address bus, active high. Typically, 8-bit processors will only use A0 to A15. Unused address lines should ideally be connected to ground but most existing modules do not have connections to these signals so they are left floating.

BUSAK	TODO

BUSRQ	TODO

CLOCK	System clock used for synchronisation so it should normally be the processor clock signal.

CLOCK2	TODO

D0 to D15	Processor data bus, active high. 8-bit processors will only used D0 to D7. Unused data lines can be left floating.

GND	Power supply ground.

HALT	TODO

INT	Interrupt request, active low. This signal should have a pull-up resistor can is pulled low by any device requesting an interrupt.

IORQ	Indicates an input/output request, active low. The Z80 has a separate address space for I/O devices but other processors will likely need to create a window in their memory map for I/O.

M1	Z80 M1 cycle, active low. This signal is very specific to the Z80 and should be pulled up for other processors.

MREQ	Indicates a memory access request, active low.

NMI	TODO

PAGE	TODO

RD	TODO

RESET	System reset signal, active low.

RFSH	TODO

RX	TODO

RX2	TODO

TX	TODO

TX2	TODO

WAIT	TODO

WR	TODO

TODO	Incomplete

## Guidance for Designers

TODO

NOTES

Recommend 74HCT levels

Jumpers on signals to signals with multiple users (pins labelled n##)

## Unresolved Issues & Notes

Possible additional signals needed: (Alan Cox)

No low/high enables to make D15-D8 actually usable

Multiple interrupt lines

DMA - BUSRQ etc

3v3 power

Are TX2 and RX2 required? (Tadeusz Pycio)

Do we need DREQ and TEND for Z180

Possibly 3v3 supply (but as Tadeusz has pointed out existing backplanes only have thin tracks on the available signal lines)

- bit data hi/lo byte enable (1 pin or 2)

Some new pins as genuine USER functions‼

Do we want a MEM_EN signal? (Tadeusz Pycio)

Better name for PAGE = RAM_EN ? (Tadeusz Pycio)

We still do not have assigned pins for the DMA service request signals. My suggestion was to use pins 78 (DREQ1) and 79 (DREQ2), but if others see the need to add DACK/EOP in addition to these signals it is worth considering another location (pins 45-48 ?)  (Tadeusz Pycio)

## Appendix A - Background

To understand what the RCBus is and why it exists, it is necessary to consider what has led us here.

In 2014 Spencer Owen created a modular version of Grant Searle’s Z80 computer design, which he called RC2014. He began selling it on Tindie and in 2016 he gave up his job and worked on RC2014 full time.

The RC2014 system attracted a community of enthusiasts, some of which made RC2014 compatible modules, as encouraged by Spencer’s website: “If your module may be of use to other RC2014 owners, please consider sharing your design or selling them yourself.  I’m happy to help you with this and to spread the word.  Note that “RC2014” is a registered trademark, so you are not allowed to call your module “RC2014 [thingy] Module” or use the RC2014 logo.  However, feel free to mark your modules as “Designed for RC2014.”

Before long there was talk of extensions to the RC2014 bus.

In 2018 the topic “New backplane -wishes ?”  led to Spencer posting the following on 17-June-2018:

“I've been musing over enhancements to the backplane for a little while now, and whilst nothing is set in stone, the pin layout would follow this;

| Enhanced | Standard |  | Enhanced | Standard |
| --- | --- | --- | --- | --- |
| A31 | 1 | 1 | A15 |  | Clock2 | 21 | 21 | Clock |
| A30 | 2 | 2 | A14 |  | BUSACK | 22 | 22 | INT |
| A29 | 3 | 3 | A13 |  | HALT | 23 | 23 | MREQ |
| A28 | 4 | 4 | A12 |  | BUSRQ | 24 | 24 | WR |
| A27 | 5 | 5 | A11 |  | WAIT | 25 | 25 | RD |
| A26 | 6 | 6 | A10 |  | NMI | 26 | 26 | IORQ |
| A25 | 7 | 7 | A9 |  | D8 | 27 | 27 | D0 |
| A24 | 8 | 8 | A8 |  | D9 | 28 | 28 | D1 |
| A23 | 9 | 9 | A7 |  | D10 | 29 | 29 | D2 |
| A22 | 10 | 10 | A6 |  | D11 | 30 | 30 | D3 |
| A21 | 11 | 11 | A5 |  | D12 | 31 | 31 | D4 |
| A20 | 12 | 12 | A4 |  | D13 | 32 | 32 | D5 |
| A19 | 13 | 13 | A3 |  | D14 | 33 | 33 | D6 |
| A18 | 14 | 14 | A2 |  | D15 | 34 | 34 | D7 |
| A17 | 15 | 15 | A1 |  | Tx2 | 35 | 35 | Tx |
| A16 | 16 | 16 | A0 |  | Rx2 | 36 | 36 | Rx |
| Gnd | 17 | 17 | Gnd |  | USR5 | 37 | 37 | USR1 |
| 5v | 18 | 18 | 5v |  | I2C SDA | 38 | 38 | IEI |
| RFSH | 19 | 19 | M1 |  | I2C SCL | 39 | 39 | IEO |
| Page | 20 | 20 | Reset |  | USR8 | 40 | 40 | USR4 |

However, on 16-June-2019 Spencer created the topic “Upcoming changes to the RC2014 bus and ecosystem“ in which he stated “RC2014 will not be changing” and further clarified this by stating “The RC2014 bus does not support IEI/IEO modules.  Through-hole components are used. And the physical bus will not be changing.”

This came as a bit of a blow to those who were looking to build on the RC2014 system and led to a discussion about how to move forward. This discussion didn’t produce any solid answers.

On 31-Jan-2023 Spencer created the topic “What has an RC2014 and a Hoover got in common?” in which he stated the following:
”RC2014 is a trademark under British law, belonging to RFC2795 Ltd (ie my company).”

“All of these kits carry the RC2014 name and RC2014 logo, and are labelled as being RFC2795 Compliant.”

“Any other kit is NOT an RC2014.”

“All sellers seem to do a very good job of making the distinction in their listings. But I don't think it is doing anybody any favours by calling a non-RC2014 machine an RC2014, least of all to the creators of compatible machines.“

This led to another discussion about the future in which it was suggested that a new name be found for products that have a degree of compatibility with RC2014 products but are not made by RFC2795 and are thus not RC2014 products. To this suggestion, Spencer wrote: “RCBus or RC80 Bus sound good to me.  It takes the essence of what the bus is without limiting it by what the RC2014 natively supports.”

Spencer’s official description of an RC2014 remains:

“RC2014 is a simple 8 bit Z80 based modular computer. It is inspired by the home built computers of the late 70s and computer revolution of the early 80s. It is not a clone of anything specific, but there are suggestions of the ZX81, UK101, S100, Superboard II and Apple I in here. It nominally has 8K ROM, 32K RAM, runs at 7.3728MHz and communicates over serial at 115,200 baud.”

Much of what some in the retro computer community wish to do with their RC2014 based systems does not match this description.

And thus the RCBus project was created.

## Appendix B - RC2014TM USER Pin Usage

The RC2014TM bus has a number of spare pins, usually called USER pins. These have been used by designers to add functions not provided by the defined bus pins. The RCBus specification attempts to maintain compatibility with the most common uses. The following is a list of some of those uses.

| Product | Pin 37 | Pin 38 | Pin 39 | Pin 40 | Pin 77 | Pin 78 | Pin 79 | Pin 80 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| RC2014 | USER1 | USER2 | USER3 | USER4 | USER5 | USER6 | USER7 | USER8 |
| BP80 | USER1 | USER2 | USER3 | IEO | USER5 | USER6 | USER7 | IEI |
| SC102 Z80 CTC | BCT3* | IEI* | IEO* |  | BCT0* | BCT1* | BCT2* |  |
| SC103 Z80 PIO |  | IEI* | IEO* |  |  |  |  |  |
| SC104 Z80 SIO/2 |  | IEI* | IEO* |  |  |  |  |  |
| SC110 SIO+CTC | CTC3* | IEI* | IEO* |  | CTC0* |  |  |  |
| SC111 Z180 CPU | INT1* |  |  |  |  |  |  |  |
| SC112 Backplane |  |  |  | IEO |  |  |  | IEI |
| SC113 Backplane |  |  |  | IEO |  |  |  | IEI |
| SC116 Backplane |  |  |  | IEO |  |  |  | IEI |
| SC126 Z180 SBC |  |  |  | IEO |  | SCL* (I2C) | SDA* (I2C) | IEI |
| SC132 Z80 SIO/0 |  | IEI* | IEO* |  |  |  |  |  |
| SC149 Z80 CPU | BUSAK* | WAIT* | BUSAK* | NMI* BUSAK* |  |  |  |  |
| Z80 CPU + CTC module (TP) | CTC3* | IEI* | IEO* |  | CTC0* |  |  |  |
| Z180 MPU (TP) | INT1* |  |  |  | INT2* |  |  |  |
| Z280 MPU (TP) | INTA* |  |  |  | INTC* |  |  |  |
| Universal SIO (TP) |  | IEI* | IEO* |  |  |  |  |  |
| DUART (TP) |  | IEI* | IEO* |  |  |  |  |  |
| 16450/550 (TP) | IRQ* |  |  |  | IRQ* |  |  |  |
| Network Controller (TP) | IRQ* |  |  |  |  |  |  |  |
| Basic & Modular Backplane 4 (TP) | USER1* | IEI*/USER2* direct or cascade | IEO*/USER3* direct or cascade | USER4 | USER5 | USER6 | USER7 | USER8 |
| 6809E/6309EP (TP) | FIRQ* | E* | RW* |  |  |  |  |  |
| 65C02 65C816 6803/6303 6808 6809/6309 68HC11 65C22 6840 65C21 (Alan Cox) | FIRQ* (some) | E* | RW* |  |  |  |  |  |
| TMS9995 (Alan Cox) | MEMEN * ? | CRUIN * ? | CRUCLK * ? |  |  |  |  |  |

* = jumpered so the end user can select if the bus pin is connected or not

| Product | Pin 37 | Pin 38 | Pin 39 | Pin 40 | Pin 77 | Pin 78 | Pin 79 | Pin 80 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PPI (Dino) | LED* | SLT_A* | CASS* | SLT_B* | OUT* |  |  |  |
| Easy-Z80 (Sergey Kiselev) |  | IEI | IEO |  |  |  |  |  |
| Z80Ctrl/CPU/IOX (JBLangston) | SCL | MISO | MOSI |  | IOXCS | AUXCS1 | AUXCS2 |  |

* = jumpered so the end user can select if the bus pin is connected or not

## Appendix C - Bus Conventions For Mapping Motorola Busses

### Introduction

The Motorola style 8-bit bus differs considerably from the bus expected by the conventional RCBus. It is possible to map from one to the other but it can be useful when integrating Motorola bus devices to make the Motorola bus signals available.

This appendix documents the existing conventions that are used for mapping a Motorola style bus to the RCBus. It is intended to be descriptive not prescriptive.

### Mapping The Bus

The following signals are mapped directly onto the RCBus from the Motorola style bus

A15-A0: 	Address bus

D0-D7: 	Data bus

INT: 	IRQ (open collector)

RESET: 	RESET (see notes section)

CLOCK: 	(see notes section)

The Motorola bus has two different signals. E is a square wave clocking the bus. During one half of the E cycle the signals change, during the other half of the E cycle the signals are valid. There is no provision

for an "idle" cycle, instead an additional read cycle is generated. This is usually targetted at a dummy location such as FFFF but some processors will generate dummy read cycles to other addresses and this can require care and is usually handled in software.

The second signal is RW. This indicates if the cycle is a read or a write using a single line unlike the 8080/Z80 bus where \RD and \RW may both be high to indicate no activity.

The Z80 style \RD and \WR signals are generated by combining the E clock with RW so that \RD or \WR goes low only when the bus state is valid.

As the Motorola bus has no notion of a separate I/O space an I/O window is normally used. By convention this is at 0xFEXX because this address window is suitable for existing operating systems for these platforms and mirrors many historic machines. There is no requirement to use 0xFEXX as the I/O

card will generally only decode the low 8-bits of the address bus anyway.

The two signals for controlling the cycle type on the Z80 bus are \MREQ for a memory request and \IORQ for an I/O request. These can be generated by decoding the upper bits of the address generated by the processor when the bus is valid.

The final 40-pin RCBUS signal is /M1. This has no equivalent on Motorola bus processors as it is used as part of the Z80 interrupt decode not just as an indication of instruction start. The current cards pull this high so that the peripheral cards do not decode bus activity as a Z80 interrupt cycle.

### Mapping The Extended Bus

The extended bus provides A23-A16, which are directly equivalent to A23-A16 on the 65C816 card.

The extended bus provides several signals that have no easy mapping. These are /BUSRQ /BUSACK and /HALT. None of these signals are used by most peripheral cards except specialist cards such as the Z80 DMA interface.

The other two signals mostly map. The \NMI signal is equivalent to the \NMI signal on Motorola bus systems (called XIRQ on some processors). The /WAIT signal is near enough the same semantics as the Z80 one that it can be provided except on the 6309E/6809E which do not support clock stretching

this way as they are intended to run synchronously with a SAM or similar device on the other half of the E cycle.

### Additional Signals

Some Motorola bus peripherals are complicated (or near impossible) to operate without the Motorola bus signals. At other times it is just useful to reduce chip count to have access.

Existing Motorola bus processor cards can provide the E RW and \FIRQ signals on bus pins. Jumpers should be used as the lines are intended to be available to the user for other purposes if desired.

37 	|   \FIRQ  	|  Open collector, pull up on CPU card

38 	|   E      		|  E clock

39 	|   RW     	|  RW signal from processor

Using these signals on a peripheral device makes the peripheral card incompatible with the basic RCbus. There is a trade-off between the convenience and simplicity of interfacing and the compatibility.

### Notes

#### Reset

The reset signal on many classic RCbus boards is very poor. The original RC2014TM systems in particular lack a proper reset controller. The Motorola bus devices that need a clean reset (such as the 68HC11) should include their own reset controller to clean up the reset during power on.

#### Clock

The conventional RCbus clock was 7.372MHz. This is also conveniently a clock that generates good serial signals and a bit under 2MHz E clock for 63xx/68xx processors. There is no requirement to use this clock, but it does improve compatibility. For slower parts half this clock is similarly convenient.

The 6502 processor clock input and E clock are the same barring skew. This effectively means a 2MHz 6502 has the same timing requirements as the 7.37MHz Z80. Whilst the RCbus can be run with a high speed 65C02 or 65C816 part it will be necessary to use 74AHCT parts in general, and even then some of the standard boards such as the 512K/512K memory card will be too slow to go above about 8MHz.

#### Bus Hold

68xx and 63xx series devices have a bus hold time (the time that signals remain valid on the data and address bus after \WR rises) that is broadly compatible with the Z80 timings used on the bus. The "classic" 6502 and 65C02 parts likewise do. Modern 65C02 and 65C816 parts have almost no bus

hold. On a backplane it becomes necessary for the processor card to cut the \WR signal early in order to produce a bus hold, otherwise many RCbus cards will not work.

#### Signal Bounce and Buffering

Some of the NMOS parts generate significant ground bounce when the address bus changes if they are driving a load with significant capacitance - such as an RCbus backplane. In these cases it may be wise to buffer the signals. Buffering signals from NMOS parts also improves compatibility with standard RCbus cards. This is not normally a problem when driving 74HCT series parts, but can be for driving other things directly (such as the CF adapter).

#### Memory Layout

The 63/68xx and 65xx parts require ROM is present at the top rather than bottom of memory at boot. The classic 512/512K card provides this, whilst the standard 'flat' 512/512K cards have a jumper to switch the RAM/ROM over.

# Footnotes

RC2014 is a trademark under British law, belonging to RFC2795 Ltd (Spencer Owen’s company)