RCBus Specification

Pre-release

for review and feedback

Version 0.0.003
27-February-2023

Introduction	3

Backplanes and Modules	4

Bus Connectors	5

Bus Pin Assignments	6

Bus Signals	8

Common Signals	8

RCBus-2014	9

RCBus-Z80	9

RCBus-68xx	10

RCBus-9995	10

Guidance for Designers	11

Sub-specification specific signals	11

Address bus	11

Memory map	11

Unresolved Issues & Notes	12

Appendix A - Background	13

Appendix B - RC2014TM USER Pin Usage	15

Appendix C - Bus Conventions For Mapping Motorola Busses	17

Introduction	17

Mapping The Bus	17

Mapping The Extended Bus	17

Additional Signals	18

Notes	18

## Introduction

The documentation describes the Retro Computer Bus (RCBus).

The RCBus is an extended version of the RC2014TM bus.

The RCBus has been created for the following reasons:

- To help distinguish RC2014TM products from products that are not RC2014TM but that claim a degree of compatibility with RC2014TM

- To reduce the chances of trademark infringement

- To help members of the retro computer community share designs and sell products based on the RC2014TM bus

- To specify a common approach to supporting features not provided by the RC2014TM bus

- To specify a common approach to supporting processors other than the Z80

Appendix A provides some background information which should help explain the above list of reasons for creating the RCBus.

The RCBus has a common backplane but some of the signals are not required for some use cases and some signals have different functions depending on the processor and other factors. Modules connected to the backplane can either work with all other RCBus modules or, more likely, a sub-set of RCBus modules.

To indicate which modules are compatible with each other, a number of sub-specifications are documented, such as:

- RCBus-2014		This is the RC2014TM specification (see www.rc2014.co.uk)

  - RCBus-2014-s	RC2014TM standard (40-pin) bus

  - RCBus-2014-e	RC2014TM enhanced (>40-pin) bus

- RCBus-Z80		Includes extensions to support advanced Z80 and Z180 family features

- RCBus-68xx		Includes extensions to support the Motorola bus style processors

A module that only requires the RC2014TM standard 40-pin bus might be compatible with RC2014-2014-s, RCBus-2014-e, and RCBus-Z80. Of course, such a compatibility claim does not mean you can put any two “compatible” modules together and expect them to work. For example, two RC2014TM serial modules will not work due to address conflicts. What “compatible” means is the physical and electrical bus signals are compatible.

The term RCBus can be used for any design that works with the full RCBus backplane or a sub-set of the RCBus backplane.

## Backplanes and Modules

Backplanes and modules can be any size and shape, but established norms are worth following.

Below is an example of an RCBus module which has a partial second row of bus pins.

Below is an example of an RCBus backplane which has 80-pin module sockets.

## Bus Connectors

The bus connectors are low cost header pins and sockets, either single or double row with up to 40-pins in each row.

Pin length ~6mm, pitch 2.54mm

Note that the most commonly used male 1x40 angled connector has a different profile to the 2x40 connector.

Single row bus socket viewed from above:

Pin 1

Pin 40

Front										Back

Double row bus socket viewed from above:

Pin 1										Pin 40

Pin 41										Pin 80

Front										Back

## Bus Pin Assignments

Bus signals are either common to all bus specifications or specific to one or more specifications.

| Pin 1st row | RC2014TM standard | RCBus backplane | RCBus Z80 | RCBus 68xx | RCBus 9995 | Notional 16-bit CPU |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | A15 |  |  |
| 2 | A14 |  |  |
| 3 | A13 |  |  |
| 4 | A12 |  |  |
| 5 | A11 |  |  |
| 6 | A10 |  |  |
| 7 | A9 |  |  |
| 8 | A8 |  |  |
| 9 | A7 |  |  |
| 10 | A6 |  |  |
| 11 | A5 |  |  |
| 12 | A4 |  |  |
| 13 | A3 |  |  |
| 14 | A2 |  |  |
| 15 | A1 |  |  |
| 16 | A0 |  |  |
| 17 | GND |  |  |
| 18 | +5V |  |  |
| 19 | M1 |  |  |
| 20 | RESET |  |  |
| 21 | CLOCK |  |  |
| 22 | INT |  |  |
| 23 | MREQ |  |  |
| 24 | WR |  |  |
| 25 | RD |  |  |
| 26 | IORQ |  |  |
| 27 | D0 |  |  |
| 28 | D1 |  |  |
| 29 | D2 |  |  |
| 30 | D3 |  |  |
| 31 | D4 |  |  |
| 32 | D5 |  |  |
| 33 | D6 |  |  |
| 34 | D7 |  |  |
| 35 | TX |  |  |
| 36 | RX |  |  |
|  | 2014 | Backplane | Z80 | 68xx | 9995 | 16-bit |  |  |
| 37 | USER1 | n37 | INT1 | FIRQ | MEMEN | n37 |  |  |
| 38 | USER2 | n38 1 | IEI | E | CRUIN | n38 1 |  |  |
| 39 | USER3 | n39 1 | IEO | RW | CRUCLK | n39 1 |  |  |
| 40 | USER4 | n40 | n40 | n40 | n40 | n40 |  |  |

1  Backplane configurable for direct or cascade (daisy-chain) connections

Second row bus signals:

| Pin 2nd row | RC2014TM enhanced | RCBus Backplane | RCBus Z80 | RCBus 68xx | RCBus 9995 | Notional 16-bit CPU |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 41 | N/A | 3v3 |  |  |
| 42 | N/A | n42 1 | BAI | n42 | n42 | n42 |  |  |
| 43 | N/A | n43 1 | BAO | n43 | n43 | n43 |  |  |
| 44 | N/A | n44 ? USER# | n44 | n44 | n44 | n44 |  |  |
| 45 | N/A | n45 ? HiLo byte | n45 | n45 | n45 | n45 |  |  |
| 46 | N/A | n46 | n46 | n46 | n46 | n46 |  |  |
| 47 | N/A | n47 | n47 | n47 | n47 | n47 |  |  |
| 48 | N/A | n48 | n48 | n48 | n48 | n48 |  |  |
| 49 | N/A | A23 |  |  |
| 50 | N/A | A22 |  |  |
| 51 | N/A | A21 |  |  |
| 52 | N/A | A20 |  |  |
| 53 | N/A | A19 |  |  |
| 54 | N/A | A18 |  |  |
| 55 | N/A | A17 |  |  |
| 56 | N/A | A16 |  |  |
| 57 | GND |  |  |
| 58 | +5V |  |  |
| 59 | RFSH |  |  |
| 60 | PAGE |  |  |
| 61 | CLOCK2 |  |  |
| 62 | BUSACK |  |  |
| 63 | HALT |  |  |
| 64 | BUSRQ |  |  |
| 65 | WAIT |  |  |
| 66 | NMI |  |  |
| 67 | D8 |  |  |
| 68 | D9 |  |  |
| 69 | D10 |  |  |
| 70 | D11 |  |  |
| 71 | D12 |  |  |
| 72 | D13 |  |  |
| 73 | D14 |  |  |
| 74 | D15 |  |  |
| 75 | TX2 |  |  |
| 76 | RX2 |  |  |
|  | 2014 | Backplane | Z80 | 68xx | 9995 | 16-bit |  |  |
| 77 | USER5 | n77 | INT2 | n77 | n77 | n77 |  |  |
| 78 | USER6 | n78 | n78 | n78 | n78 | n78 |  |  |
| 79 | USER7 | n79 | n79 | n79 | n79 | n79 |  |  |
| 80 | USER8 | n80 | n80 | n80 | n80 | n80 |  |  |

1  Backplane configurable for direct or cascade (daisy-chain) connections

## Bus Signals

Signals are TTL level unless otherwise indicated.

### Common Signals

This section describes each of the signals common to all processor types.

Signals are defined by their function with a Z80 CPU unless otherwise stated.

+5V	Power supply +5 volts, recommended tolerance +/-0.25 volts.

+3V3	Power supply +3.3 volts. Optional.

A0 to A23	Address bus, output from CPU, active high, tristate. Typically, 8-bit processors will only use A0 to A15.

BUSAK	Bus acknowledge, output from CPU, active low. The CPU outputs a low on this line indicating the address bus, data bus, and control signals MREQ, IORQ, RD, and WR have entered their high-impedance states.

BUSRQ	Bus request, input to CPU, active low. This is pulled low by a device that wants to take control on the CPU’s address, data and control bus.

CLOCK	Clock, input to CPU. System clock used for synchronisation so it should normally be the CPU clock signal.

CLOCK2	This is a second clock usually used as a clock source for a UART.

D0 to D15	Data bus, input/output, active high, tristate. 8-bit processors will only used D0 to D7. Unused data lines can be left floating.

GND	Power supply ground.

HALT	Halt, output from CPU, active low. This indicates the CPU has executed a HALT instruction and is waiting for an interrupt before resuming operation.

INT	Interrupt request, input to CPU, active low. This signal should have a pull-up resistor can is pulled low by any device requesting an interrupt.

IORQ	Input/output request, output from CPU, active low, tristate. The Z80 has a separate address space for I/O devices but other processors will likely need to create a window in their memory map for I/O.

M1	Machine cycle one, output from CPU, active low. 
This signal is very specific to the Z80 and should be pulled up for other processors.

MREQ	Memory request, output from CPU, active low, tristate. Indicates that the address bus holds a valid address for a memory read or a memory write operation.

NMI	Non-maskable interrupt, input to CPU, active low. Negative edge triggered interrupt.

PAGE	Page RAM/ROM, active high. Low to enable ROM and disable its shadow RAM. High to disable ROM and enable its shadow RAM. For a Z80 system the ROM is at the bottom of memory (starting at address 0x0000) following reset. This signal is set high to replace this ROM with RAM, allowing a full 64k of RAM. Perhaps a better name would be RAM_ENable. There are other memory management schemes in use that do not use this signal.

RD	Read, output from CPU, active low, tristate. Indicates that the CPU wants to read data from memory or an I/O device.

RESET	Reset, input to CPU, active low. System reset signal.

RFSH	Refresh, output from CPU, active low. Indicates a memory refresh cycle.

RX	This signal is designed to allow a serial port to communicate with a device on another module. RX is an input to a serial port, such as a UART, and an output from a serial device, such as a terminal module.

RX2	A second serial communications ‘RX’ signal.

TX	This signal is designed to allow a serial port to communicate with a device on another module. TX is an output from a serial port, such as a UART, and an input to a serial device, such as a terminal module.

TX2	A second serial communications ‘TX’ signal.

WAIT	Wait, input to CPU, active low. Communicates to the CPU that the addressed memory or I/O devices are not ready for a data transfer. The CPU continues to enter a WAIT state as long as this signal is active.

WR	Write, output from CPU, active low, tristate. Indicates that the CPU wants to write data to memory or an I/O device.

### RCBus-2014

The following are signals specific to the basic RC2014TM bus specification.

USER#	Signals USER1 to USER8 are free for the user to do as they please.

### RCBus-Z80

The following are signals specific to systems using the Z80 family bus specification. Eg. Z80 and Z180.

BAI	Bus acknowledge in, input, active low. BAI and BAO form a direct memory access priority daisy-chain. BAI signals that the system buses have been released for DMA control.

BAO	Bus acknowledge out, output, active low. BAI and BAO form a direct memory access priority daisy-chain. BAO signals that the CPU has relinquished control of the bus.

IEI	Interrupt enable in, input to an interrupt generating device, active high. IEI and IEO form an interrupt priority daisy-chain. A high on IEI indicates that no other device of higher priority is interrupting.

IEO	Interrupt enable out, output from an interrupt generating device, active high. IEI and IEO form an interrupt priority daisy-chain. IEO is high only when IEI is high and this device is not requesting an interrupt.

INT1	Interrupt, input to CPU, active low.

INT2	Interrupt, input to CPU, active low.

n##	Reserved

### RCBus-68xx

The following are signals specific to systems using the 68xx, 63xx and 65xx family bus specification.

FIRQ	Fast interrupt request, input to CPU, active low.

E	Data bus enable, input to CPU, active high.

RW	Read/write, output from CPU. High for read operations, low for write operations.

n##	Reserved

### RCBus-9995

The following are signals specific to systems using the TMS9995 family bus specification.

CRUCLK	CRU clock, output from CPU, active low.

CRUIN	CRU input data,input to CPU, active high.

MEMEN	Memory enable, output from CPU, active low.

n##	Reserved

## Guidance for Designers

The basic idea is that all processor types generate the common bus signals, essentially Z80 compatible signals, where ever possible. Any additional processor or sub-specification specific signals are optional. This approach is designed to give the greatest compatibility across all uses of the RCBus.

It is recommended that CMOS ICs be used wherever possible and that 74HCT series ICs are used rather than other 74 series families.

For further guidance on processor specific issues and sub-specification specific issues, see the appropriate appendix.

### Sub-specification specific signals

It is recommended that jumper options be provided on modules for connections to the sub-specification specific signals. Namely, pins 37 to 40, 77 to 80, and 42 to 48.

??? should this only be the traditional USER pins? (ie. 37 to 40, and 77 to 80)

### Address bus

Unused address lines should ideally be pulled down with weak pulled down resistors to enable CPU and memory modules to be used together even if there is a mismatch in the number of address lines used.

### Memory map

Some processors require boot ROMs to be at the top of memory and others at the bottom of memory. It is recommended that memory modules provide an option for this.

Some processors have separate address spaces for I/O devices and some require them to be mapped as memory. Memory modules designed to work with different processors will need to allow for this.

Processors that do not have separate I/O address spaces should generate the RCBus IOREQ signal when I/O addresses are decoded and also ensure the MREQ signal is not active at these times.

## Unresolved Issues & Notes

Possible additional signals needed: (Alan Cox)

No low/high enables to make D15-D8 actually usable

Multiple interrupt lines

DMA - BUSRQ etc

3v3 power

Are TX2 and RX2 required? (Tadeusz Pycio)

Do we need DREQ and TEND for Z180

Possibly 3v3 supply (but as Tadeusz has pointed out existing backplanes only have thin tracks on the available signal lines)

- bit data hi/lo byte enable (1 pin or 2)

Some new pins as genuine USER functions‼

Do we want a MEM_EN signal? (Tadeusz Pycio)

Better name for PAGE = RAM_EN ? (Tadeusz Pycio)

We still do not have assigned pins for the DMA service request signals. My suggestion was to use pins 78 (DREQ1) and 79 (DREQ2), but if others see the need to add DACK/EOP in addition to these signals it is worth considering another location (pins 45-48 ?)  (Tadeusz Pycio)

## Appendix A - Background

To understand what the RCBus is and why it exists, it is necessary to consider what has led us here.

In 2014 Spencer Owen created a modular version of Grant Searle’s Z80 computer design, which he called RC2014. He began selling it on Tindie and in 2016 he gave up his job and worked on RC2014 full time.

The RC2014 system attracted a community of enthusiasts, some of which made RC2014 compatible modules, as encouraged by Spencer’s website: “If your module may be of use to other RC2014 owners, please consider sharing your design or selling them yourself.  I’m happy to help you with this and to spread the word.  Note that “RC2014” is a registered trademark, so you are not allowed to call your module “RC2014 [thingy] Module” or use the RC2014 logo.  However, feel free to mark your modules as “Designed for RC2014.”

Before long there was talk of extensions to the RC2014 bus.

In 2018 the topic “New backplane -wishes ?”  led to Spencer posting the following on 17-June-2018:

“I've been musing over enhancements to the backplane for a little while now, and whilst nothing is set in stone, the pin layout would follow this;

| Enhanced | Standard |  | Enhanced | Standard |
| --- | --- | --- | --- | --- |
| A31 | 1 | 1 | A15 |  | Clock2 | 21 | 21 | Clock |
| A30 | 2 | 2 | A14 |  | BUSACK | 22 | 22 | INT |
| A29 | 3 | 3 | A13 |  | HALT | 23 | 23 | MREQ |
| A28 | 4 | 4 | A12 |  | BUSRQ | 24 | 24 | WR |
| A27 | 5 | 5 | A11 |  | WAIT | 25 | 25 | RD |
| A26 | 6 | 6 | A10 |  | NMI | 26 | 26 | IORQ |
| A25 | 7 | 7 | A9 |  | D8 | 27 | 27 | D0 |
| A24 | 8 | 8 | A8 |  | D9 | 28 | 28 | D1 |
| A23 | 9 | 9 | A7 |  | D10 | 29 | 29 | D2 |
| A22 | 10 | 10 | A6 |  | D11 | 30 | 30 | D3 |
| A21 | 11 | 11 | A5 |  | D12 | 31 | 31 | D4 |
| A20 | 12 | 12 | A4 |  | D13 | 32 | 32 | D5 |
| A19 | 13 | 13 | A3 |  | D14 | 33 | 33 | D6 |
| A18 | 14 | 14 | A2 |  | D15 | 34 | 34 | D7 |
| A17 | 15 | 15 | A1 |  | Tx2 | 35 | 35 | Tx |
| A16 | 16 | 16 | A0 |  | Rx2 | 36 | 36 | Rx |
| Gnd | 17 | 17 | Gnd |  | USR5 | 37 | 37 | USR1 |
| 5v | 18 | 18 | 5v |  | I2C SDA | 38 | 38 | IEI |
| RFSH | 19 | 19 | M1 |  | I2C SCL | 39 | 39 | IEO |
| Page | 20 | 20 | Reset |  | USR8 | 40 | 40 | USR4 |

However, on 16-June-2019 Spencer created the topic “Upcoming changes to the RC2014 bus and ecosystem“ in which he stated “RC2014 will not be changing” and further clarified this by stating “The RC2014 bus does not support IEI/IEO modules.  Through-hole components are used. And the physical bus will not be changing.”

This came as a bit of a blow to those who were looking to build on the RC2014 system and led to a discussion about how to move forward. This discussion didn’t produce any solid answers.

On 31-Jan-2023 Spencer created the topic “What has an RC2014 and a Hoover got in common?” in which he stated the following:
”RC2014 is a trademark under British law, belonging to RFC2795 Ltd (ie my company).”

“All of these kits carry the RC2014 name and RC2014 logo, and are labelled as being RFC2795 Compliant.”

“Any other kit is NOT an RC2014.”

“All sellers seem to do a very good job of making the distinction in their listings. But I don't think it is doing anybody any favours by calling a non-RC2014 machine an RC2014, least of all to the creators of compatible machines.“

This led to another discussion about the future in which it was suggested that a new name be found for products that have a degree of compatibility with RC2014 products but are not made by RFC2795 and are thus not RC2014 products. To this suggestion, Spencer wrote: “RCBus or RC80 Bus sound good to me.  It takes the essence of what the bus is without limiting it by what the RC2014 natively supports.”

Spencer’s official description of an RC2014 remains:

“RC2014 is a simple 8 bit Z80 based modular computer. It is inspired by the home built computers of the late 70s and computer revolution of the early 80s. It is not a clone of anything specific, but there are suggestions of the ZX81, UK101, S100, Superboard II and Apple I in here. It nominally has 8K ROM, 32K RAM, runs at 7.3728MHz and communicates over serial at 115,200 baud.”

Much of what some in the retro computer community wish to do with their RC2014 based systems does not match this description.

And thus the RCBus project was created.

## Appendix B - RC2014TM USER Pin Usage

The RC2014TM bus has a number of spare pins, usually called USER pins. These have been used by designers to add functions not provided by the defined bus pins. The RCBus specification attempts to maintain compatibility with the most common uses. The following is a list of some of those uses.

| Product | Pin 37 | Pin 38 | Pin 39 | Pin 40 | Pin 77 | Pin 78 | Pin 79 | Pin 80 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| RC2014 | USER1 | USER2 | USER3 | USER4 | USER5 | USER6 | USER7 | USER8 |
| BP80 | USER1 | USER2 | USER3 | IEO | USER5 | USER6 | USER7 | IEI |
| SC102 Z80 CTC | BCT3* | IEI* | IEO* |  | BCT0* | BCT1* | BCT2* |  |
| SC103 Z80 PIO |  | IEI* | IEO* |  |  |  |  |  |
| SC104 Z80 SIO/2 |  | IEI* | IEO* |  |  |  |  |  |
| SC110 SIO+CTC | CTC3* | IEI* | IEO* |  | CTC0* |  |  |  |
| SC111 Z180 CPU | INT1* |  |  |  |  |  |  |  |
| SC112 Backplane |  |  |  | IEO |  |  |  | IEI |
| SC113 Backplane |  |  |  | IEO |  |  |  | IEI |
| SC116 Backplane |  |  |  | IEO |  |  |  | IEI |
| SC126 Z180 SBC |  |  |  | IEO |  | SCL* (I2C) | SDA* (I2C) | IEI |
| SC132 Z80 SIO/0 |  | IEI* | IEO* |  |  |  |  |  |
| SC149 Z80 CPU | BUSAK* | WAIT* | BUSAK* | NMI* BUSAK* |  |  |  |  |
| Z80 CPU + CTC module (TP) | CTC3* | IEI* | IEO* |  | CTC0* |  |  |  |
| Z180 MPU (TP) | INT1* |  |  |  | INT2* |  |  |  |
| Z280 MPU (TP) | INTA* |  |  |  | INTC* |  |  |  |
| Universal SIO (TP) |  | IEI* | IEO* |  |  |  |  |  |
| DUART (TP) |  | IEI* | IEO* |  |  |  |  |  |
| 16450/550 (TP) | IRQ* |  |  |  | IRQ* |  |  |  |
| Network Controller (TP) | IRQ* |  |  |  |  |  |  |  |
| Basic & Modular Backplane 4 (TP) | USER1* | IEI*/USER2* direct or cascade | IEO*/USER3* direct or cascade | USER4 | USER5 | USER6 | USER7 | USER8 |
| 6809E/6309EP (TP) | FIRQ* | E* | RW* |  |  |  |  |  |
| 65C02 65C816 6803/6303 6808 6809/6309 68HC11 65C22 6840 65C21 (Alan Cox) | FIRQ* (some) | E* | RW* |  |  |  |  |  |
| TMS9995 (Alan Cox) | MEMEN * ? | CRUIN * ? | CRUCLK * ? |  |  |  |  |  |

* = jumpered so the end user can select if the bus pin is connected or not

| Product | Pin 37 | Pin 38 | Pin 39 | Pin 40 | Pin 77 | Pin 78 | Pin 79 | Pin 80 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| PPI (Dino) | LED* | SLT_A* | CASS* | SLT_B* | OUT* |  |  |  |
| Easy-Z80 (Sergey Kiselev) |  | IEI | IEO |  |  |  |  |  |
| Z80Ctrl/CPU/IOX (JBLangston) | SCL | MISO | MOSI |  | IOXCS | AUXCS1 | AUXCS2 |  |

* = jumpered so the end user can select if the bus pin is connected or not

## Appendix C - Bus Conventions For Mapping Motorola Busses

### Introduction

The Motorola style 8-bit bus differs considerably from the bus expected by the conventional RCBus. It is possible to map from one to the other but it can be useful when integrating Motorola bus devices to make the Motorola bus signals available.

This appendix documents the existing conventions that are used for mapping a Motorola style bus to the RCBus. It is intended to be descriptive not prescriptive.

### Mapping The Bus

The following signals are mapped directly onto the RCBus from the Motorola style bus

A15-A0: 	Address bus

D0-D7: 	Data bus

INT: 	IRQ (open collector)

RESET: 	RESET (see notes section)

CLOCK: 	(see notes section)

The Motorola bus has two different signals. E is a square wave clocking the bus. During one half of the E cycle the signals change, during the other half of the E cycle the signals are valid. There is no provision

for an "idle" cycle, instead an additional read cycle is generated. This is usually targetted at a dummy location such as FFFF but some processors will generate dummy read cycles to other addresses and this can require care and is usually handled in software.

The second signal is RW. This indicates if the cycle is a read or a write using a single line unlike the 8080/Z80 bus where \RD and \RW may both be high to indicate no activity.

The Z80 style \RD and \WR signals are generated by combining the E clock with RW so that \RD or \WR goes low only when the bus state is valid.

As the Motorola bus has no notion of a separate I/O space an I/O window is normally used. By convention this is at 0xFEXX because this address window is suitable for existing operating systems for these platforms and mirrors many historic machines. There is no requirement to use 0xFEXX as the I/O

card will generally only decode the low 8-bits of the address bus anyway.

The two signals for controlling the cycle type on the Z80 bus are \MREQ for a memory request and \IORQ for an I/O request. These can be generated by decoding the upper bits of the address generated by the processor when the bus is valid.

The final 40-pin RCBUS signal is /M1. This has no equivalent on Motorola bus processors as it is used as part of the Z80 interrupt decode not just as an indication of instruction start. The current cards pull this high so that the peripheral cards do not decode bus activity as a Z80 interrupt cycle.

### Mapping The Extended Bus

The extended bus provides A23-A16, which are directly equivalent to A23-A16 on the 65C816 card.

The extended bus provides several signals that have no easy mapping. These are /BUSRQ /BUSACK and /HALT. None of these signals are used by most peripheral cards except specialist cards such as the Z80 DMA interface.

The other two signals mostly map. The \NMI signal is equivalent to the \NMI signal on Motorola bus systems (called XIRQ on some processors). The /WAIT signal is near enough the same semantics as the Z80 one that it can be provided except on the 6309E/6809E which do not support clock stretching

this way as they are intended to run synchronously with a SAM or similar device on the other half of the E cycle.

### Additional Signals

Some Motorola bus peripherals are complicated (or near impossible) to operate without the Motorola bus signals. At other times it is just useful to reduce chip count to have access.

Existing Motorola bus processor cards can provide the E RW and \FIRQ signals on bus pins. Jumpers should be used as the lines are intended to be available to the user for other purposes if desired.

37 	|   \FIRQ  	|  Open collector, pull up on CPU card

38 	|   E      		|  E clock

39 	|   RW     	|  RW signal from processor

Using these signals on a peripheral device makes the peripheral card incompatible with the basic RCbus. There is a trade-off between the convenience and simplicity of interfacing and the compatibility.

### Notes

#### Reset

The reset signal on many classic RCbus boards is very poor. The original RC2014TM systems in particular lack a proper reset controller. The Motorola bus devices that need a clean reset (such as the 68HC11) should include their own reset controller to clean up the reset during power on.

#### Clock

The conventional RCbus clock was 7.372MHz. This is also conveniently a clock that generates good serial signals and a bit under 2MHz E clock for 63xx/68xx processors. There is no requirement to use this clock, but it does improve compatibility. For slower parts half this clock is similarly convenient.

The 6502 processor clock input and E clock are the same barring skew. This effectively means a 2MHz 6502 has the same timing requirements as the 7.37MHz Z80. Whilst the RCbus can be run with a high speed 65C02 or 65C816 part it will be necessary to use 74AHCT parts in general, and even then some of the standard boards such as the 512K/512K memory card will be too slow to go above about 8MHz.

#### Bus Hold

68xx and 63xx series devices have a bus hold time (the time that signals remain valid on the data and address bus after \WR rises) that is broadly compatible with the Z80 timings used on the bus. The "classic" 6502 and 65C02 parts likewise do. Modern 65C02 and 65C816 parts have almost no bus

hold. On a backplane it becomes necessary for the processor card to cut the \WR signal early in order to produce a bus hold, otherwise many RCbus cards will not work.

#### Signal Bounce and Buffering

Some of the NMOS parts generate significant ground bounce when the address bus changes if they are driving a load with significant capacitance - such as an RCbus backplane. In these cases it may be wise to buffer the signals. Buffering signals from NMOS parts also improves compatibility with standard RCbus cards. This is not normally a problem when driving 74HCT series parts, but can be for driving other things directly (such as the CF adapter).

#### Memory Layout

The 63/68xx and 65xx parts require ROM is present at the top rather than bottom of memory at boot. The classic 512/512K card provides this, whilst the standard 'flat' 512/512K cards have a jumper to switch the RAM/ROM over.

# Footnotes

RC2014 is a trademark under British law, belonging to RFC2795 Ltd (Spencer Owen’s company)