// This file is part of MatrixPilot.

//

//    http://code.google.com/p/gentlenav/

//

// Copyright 2009-2012 MatrixPilot Team

// See the AUTHORS.TXT file for a list of authors of MatrixPilot.

//

// MatrixPilot is free software: you can redistribute it and/or modify

// it under the terms of the GNU General Public License as published by

// the Free Software Foundation, either version 3 of the License, or

// (at your option) any later version.

//

// MatrixPilot is distributed in the hope that it will be useful,

// but WITHOUT ANY WARRANTY; without even the implied warranty of

// MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE.  See the

// GNU General Public License for more details.

//

// You should have received a copy of the GNU General Public License

// along with MatrixPilot.  If not, see <http://www.gnu.org/licenses/>.

////////////////////////////////////////////////////////////////////////////////

// UDB LOGO Waypoint handling

// Move on to the next waypoint when getting within this distance of the current goal (in meters)

#define WAYPOINT_RADIUS 		25

// Origin Location

// When using relative waypoints, the default is to interpret those waypoints as relative to the

// plane's power-up location.  Here you can choose to use any specific, fixed 3D location as the

// origin point for your relative waypoints.

//

// USE_FIXED_ORIGIN should be 0 to use the power-up location as the origin for relative waypoints.

// Set it to 1 to use a fixed location as the origin, no matter where you power up.

// FIXED_ORIGIN_LOCATION is the location to use as the origin for relative waypoints.  It uses the

// format { X, Y, Z } where:

// X is Logitude in degrees * 10^7

// Y is Latitude in degrees * 10^7

// Z is altitude above sea level, in meters, as a floating point value.

//

// If you are using waypoints for an autonomous landing, it is a good idea to set the altitude value

// to be the altitude of the landing point, and then express the heights of all of the waypoints with

// respect to the landing point.

// If you are using OpenLog, an easy way to determine the altitude of your landing point is to

// examine the telemetry after a flight, take a look in the .csv file, it will be easy to spot the

// altitude, expressed in meters.

#define USE_FIXED_ORIGIN		0

// #define FIXED_ORIGIN_LOCATION	{ -1219950467, 374124664, 2.00 }	// A point in Baylands Park in Sunnyvale, CA

// #define FIXED_ORIGIN_LOCATION	{ -797866871, 435341708, 182.0 }	// North Field field center launch point 168m above sea lev

// #define FIXED_ORIGIN_LOCATION	{-797279923, 434894384, 170.0  }	// OMFC South Field field NW offset DC

#define FIXED_ORIGIN_LOCATION	{-797278708, 434893087, 170.0}			// OMFC South Field field dead center

// #define FIXED_ORIGIN_LOCATION	{-801586991, 429692064, 226.2 }		// Bennet Field, Springvale East field

// #define FIXED_ORIGIN_LOCATION	{-801605927, 429691278, 226.2 }		// Bennet Field, Springvale West field

// #define FIXED_ORIGIN_LOCATION	{-801595895, 429693672,  226.2}		// Bennet Field, Springvale Center field

// #define FIXED_ORIGIN_LOCATION	{-801595895, 429693672,  226.2}		// Bennet Field, Springvale Center field

////////////////////////////////////////////////////////////////////////////////

// UDB LOGO Flight Planning definitions

//

// The UDB Logo flight plan language lets you use a language similar to Logo, aka Turtle graphics, to

// control your plane.  You are commanding an imaginary "turtle" to move to specific locations, and the

// plane will head towards the turtle.

//

// You can also control the camera targeting code by switching from the plane turtle, to the camera turtle

// by using the SET_TURTLE(CAMERA) command.  Then logo commands will move the location that the camera

// is targeting, instead of the location to aim the plane.

//

// Each time you enter waypoint mode, the state is reset and your logo program starts from the top.  If

// you enter RTL mode, the state is reset and your rtlInstructions[] logo program is run instead.

// The following state is cleared when entering waypoint mode or RTL mode: (but not when your program

// ends and starts over)

//   - The plane turtle and camera turtle begin at the plane's current position and altitude.

//   - Both turtles begin pointing in the plane's current heading.

//   - The flags are all turned off.

//   - The pen is down, and the PLANE turtle is active.

//

// To use UDB Logo, set FLIGHT_PLAN_TYPE to FP_LOGO in options.h.

////////////////////////////////////////////////////////////////////////////////

// Commands

//

// Use the following commands to create your logo paths:

//

// HOME				- Return the turtle to the origin, aiming North.

//

// FD(x)			- Move the turtle forward x meters, in the turtle's current direction.

// BK(x)			- Move the turtle backwards x meters, in the turtle's current direction.

// USE_CURRENT_POS	- Move the turtle to the plane's current {X,Y} position.  Mostly useful

//					  while being sneaky using PEN_UP.

// RT(x)			- Rotate the turtle to the right by x degrees.

// LT(x)			- Rotate the turtle to the left by x degrees.

// SET_ANGLE(x)		- Set the turtle to point x degrees clockwise from N.

// USE_CURRENT_ANGLE- Aim the turtle in the direction that the plane is currently headed.

// USE_ANGLE_TO_GOAL- Aim the turtle in the direction of the goal from the location of the plane.

// EAST(x)			- Move the turtle x meters East.

// WEST(x)			- Move the turtle x meters West.

// SET_X_POS(x)		- Set the X value of the turtle (meters East of the origin) to x.

//

// NORTH(y)			- Move the turtle y meters North.

// SOUTH(y)			- Move the turtle y meters South.

// SET_Y_POS(y)		- Set the Y value of the turtle (meters North of the origin) to y.

//

// SET_POS(x, y)	- Set both x and y at the same time.

// SET_ABS_POS(x, y)- Set absolute X,Y location (long,lat) in degrees * 10^7

// ALT_UP(z)		- Gain z meters of altitude.

// ALT_DOWN(z)		- Drop z meters of altitude.

// SET_ALT(z)		- Set altitude to z.

// SPEED_INCREASE(x)- Increases the target speed by x m/s

// SPEED_DECREASE(x)- Decreases the target speed by x m/s

// SET_SPEED(x)		- Sets the target speed to x m/s

// REPEAT(n)		- Repeat all of the instructions until the matching END, n times

// REPEAT_FOREVER	- Repeat all of the instructions until the matching END, forever

// END				- End the current REPEAT loop or Subroutine definition

// IF_EQ(val, x)	- Looks up a system value (listed below) and checks if it's equal to x.

// 					  If so, runs commands until reaching ELSE or END.  If not, skips to ELSE

//					  and runs until END, or just skips to END if there's no ELSE.

//					  Available IF commands: IF_EQ(equal), IF_NE(not equal),

//					  IF_GT(val>x), IF_LT(val<x),IF_GE(val>=x), IF_LE(val<=x).

// ELSE				- Starts a list of commands that get run if the preceding IF failed.

// PEN_UP			- While the pen is up, logo code execution does not stop to wait for the

// 					  plane to move to each new position of the turtle before continuing.

//					  This allows you to use multiple logo instructions to get the turtle to

//					  the next goal location before commanding the plane to fly there by

//					  putting the pen back down.

// PEN_DOWN			- When the pen is down, the plane moves to each new position of the turtle

//					  before more logo instructions are interpereted.

// PEN_TOGGLE		- Toggle the pen between up and down.

// SET_TURTLE(T)	- Choose to control either the plane's turtle, or the camera turtle.

//					  Use either SET_TURTLE(PLANE) or SET_TURTLE(CAMERA).

// Commands for Modifying Flags

//

// FLAG_ON(F)		- Turn on flag F.  (See below for a list of flags.)

// FLAG_OFF(F)		- Turn off flag F.

// FLAG_TOGGLE(F)	- Toggle flag F.

//

// The supported flags are the following:

//

// F_TAKEOFF		- More quickly gain altitude at takeoff.

// F_INVERTED		- Fly with the plane upside down. (only if STABILIZE_INVERTED_FLIGHT is set to 1 in options.h)

// F_HOVER			- Hover the plane with the nose up. (only if STABILIZE_HOVER is set to 1 in options.h)

//					  NOTE: while hovering, no navigation is performed, and throttle is under manual control.

// F_TRIGGER		- Trigger an action to happen at this point in the flight.  (See the Trigger Action section of the options.h file.)

// F_ALTITUDE_GOAL	- Climb or descend to the given altitude.

// F_CROSS_TRACK	- Navigate using cross-tracking.  Best used for longer flight legs.

// F_LAND			- Fly with the throttle off.

// Commands for Creating and Calling Subroutines

//

// TO(FUNC)			- Begin defining subroutine FUNC (requires #define FUNC N where N is an

//					  integer, unique among your defined subroutines.  End each subroutine

//					  definition with an END.

// DO(FUNC)			- Run subroutine FUNC.  When it finishes, control returns to the line after

//					  the DO() instruction.

// EXEC(FUNC)		- Call FUNC as though it were the beginning of the logo program.  This will never return.

//					  When/if FUNC finishes, logo will start back at the beginning of the program.

// DO_ARG(FUNC, PARAM) - Run subroutine FUNC, using an integer value as a parameter.

// EXEC_ARG(FUNC, PARAM) - Exec subroutine FUNC, using an integer value as a parameter.

//

// FD_PARAM			- From within a subroutine, call the FD command using the parameter

//					  passed to this subroutine as the distance.

// RT_PARAM			- From within a subroutine, call the RT command using the parameter

//					  passed to this subroutine as the angle.

// REPEAT_PARAM		- Start a REPEAT block, using the current subroutine's parameter as the

//					  number of times to repeat.

// DO_PARAM(FUNC)	- Call subroutine FUNC with a parameter equal to the current subroutine's

//					  parameter value.

//

// PARAM_ADD(x)		- Adds x to the current subroutine's current parameter value.  Fun

//					  inside repeats inside subroutines!

// PARAM_SUB(x)		- Subtracts x from the current subroutine's current parameter value.

// PARAM_MUL(x)		- Multiplies the current subroutine's current parameter value by x.

// PARAM_DIV(x)		- Divides the current subroutine's current parameter value by x.

// PARAM_SET(x)		- Sets the current subroutine's current parameter value to x.

//

// LOAD_TO_PARAM(val) - Loads a system value (listed below) into the current subroutine's parameter value.

//

// All parameter-related commands:

//		FD_PARAM, BK_PARAM, RT_PARAM, LT_PARAM, SET_ANGLE_PARAM,

//		EAST_PARAM, WEST_PARAM, NORTH_PARAM, SOUTH_PARAM, ALT_UP_PARAM, ALT_DOWN_PARAM,

//		SET_X_POS_PARAM, SET_Y_POS_PARAM, SET_ALT_PARAM,

//		SPEED_INCREASE_PARAM, SPEED_DECREASE_PARAM, SET_SPEED_PARAM

//		REPEAT_PARAM, DO_PARAM(FUNC), EXEC_PARAM(FUNC)

//		PARAM_SET(x), PARAM_ADD(x), PARAM_SUB(x), PARAM_MUL(x), PARAM_DIV(x)

//		IF_EQ_PARAM(x), IF_NE_PARAM(x), IF_GT_PARAM(x), IF_LT_PARAM(x), IF_GE_PARAM(x), IF_LE_PARAM(x)

// SET_INTERRUPT(f) - Sets a user-defined logo function to be called at 40Hz.  Be careful not to modify

//					  the turtle location from within your interrupt function unless you really want to!

//					  Usually you'll just want your interrupt function to check some condition, and do

//					  something only if it's true.  (Like fly home only if you get too far away.)

// CLEAR_INTERRUPT	- Clears/disables the interrupt function.  Not usually needed.

// System Values for use with LOAD_TO_PARAM(val) and IF_XX() commands

//

// DIST_TO_HOME			- in m

// DIST_TO_GOAL			- in m

// ALT					- in m

// ALT_SONAR			- in cm use only for UDB4 with sonar

// CURRENT_ANGLE		- in degrees. 0-359 (clockwise, 0=North)

// ANGLE_TO_HOME		- in degrees. 0-359 (clockwise, 0=North)

// ANGLE_TO_GOAL		- in degrees. 0-359 (clockwise, 0=North)

// REL_ANGLE_TO_HOME	- in degrees. -180-179 (0=heading directly towards home. clockwise offset is positive)

// REL_ANGLE_TO_GOAL	- in degrees. -180-179 (0=heading directly towards goal. clockwise offset is positive)

// GROUND_SPEED			- in cm/s

// AIR_SPEED			- in cm/s

// AIR_SPEED_Z			- in cm/s

// WIND_SPEED			- in cm/s

// WIND_SPEED_X			- in cm/s

// WIND_SPEED_Y			- in cm/s

// WIND_SPEED_Z			- in cm/s

// PARAM				- current param value

// XX_INPUT_CHANNEL		- channel value from 2000-4000 (any channel defined in options.h, e.g. THROTTLE_INPUT_CHANNEL)

////////////////////////////////////////////////////////////////////////////////

// Notes:

//	- Altitudes are relative to the starting point, and the initial altitude goal is 100 meters up.

//	- All angles are in degrees.

//	- Repeat commands and subroutines can be nested up to 12-deep.

//	- If the end of the list of instructions is reached, we start over at the top from the current location and angle.

//    This does not take up one of the 12 nested repeat levels.

//	- If you use many small FD() commands to make curves, I suggest enabling cross tracking: FLAG_ON(F_CROSS_TRACK)

//	- All Subroutines have to appear after the end of your main logo program.

////////////////////////////////////////////////////////////////////////////////

// Define the main flight plan as:

//

// #define FOO 1

//

// const struct logoInstructionDef instructions[] = {

//		instruction1

//		instruction2

//		etc.

//		END

//

//		TO (FOO)

//			etc.

//		END

//	} ;

//

// and the Failsafe RTL course as:

//

// #define BAR 2

//

// const struct logoInstructionDef rtlInstructions[] = {

//		instruction1

//		instruction2

//		etc.

//		END

//

//		TO (BAR)

//			etc.

//		END

//	} ;

////////////////////////////////////////////////////////////////////////////////

// Main Flight Plan

//

////////////////////////////////////////////////////////////////////////////////

// Main Flight Plan

~~~

//////  COMMON FUNCTIONS  //////

~~~

#define CM_AUTOLAND			19

#define CM_LAND_SONAR			20

#define CM_DIST_RETTOHOME			21

// //////  PARAMETERS  //////

~~~

#define PM_TKOFF_SNRALT			300  // cm, takeoff sonar low alt. threshold

#define PM_TKOFF_GPSALT			3      // m, takeoff GPS low alt. threshold

#define PM_SRNDTURN_FD			10   // m

//  LANDING

#define PM_LANDG_SPAN			200  // m, landing, approach to sonar managed soft touch-down

#define PM_LANDG_APRCH_GPSALT	   3   // m, start of landing field LT/min. alt. threshold

#define PM_LANDG_APRCH_SNRALT	300  // cm, start of landing field sonar LT/min. alt. threshold

#define PM_LANDG_FSTSEG_SNRALT     280  // cm, FIRST SEGMENT landing sonar alt. threshold

#define PM_LANDG_SECSEG_SNRALT    180  // cm, SECOND SEGMENT landing sonar alt. threshold

#define PM_LANDG_TRDSEG_SNRALT      80  // cm, THIRD SEGMENT landing sonar alt. threshold

#define PM_LANDG_FSTSEG_GPSALT         3  // m, FIRST SEGMENT landing sonar alt. threshold

#define PM_LANDG_SECSEG_GPSALT        2   // m, SECOND SEGMENT landing sonar alt. threshold

#define PM_LANDG_TRDSEG_GPSALT 	   1   // m, THIRD SEGMENT landing sonar alt. threshold

#define PM_LANDG_APCHSEG_FD  	   2  // m, END OF LANDING APPROACH FLARE-FD distance

#define PM_LANDG_FSTSEG_FD  	   3  // m, FIRST SEGMENT landing FLARE-FD distance

#define PM_LANDG_SECSEG_FD  	   3   // m, SECOND SEGMENT landing FLARE-FD distance

#define PM_LANDG_TRDSEG_FD	   2    // m, THIRD SEGMENT landing FLARE-FD distance

//  SPEED control 9 32.4kph, 10 36kph, 11 39.6kph, 12 43.2kph, 13 46.8kph

#define PM_SPEED_LOWTRH		   9    // m/sec, speed LT/min. alt. threshold

#define PM_SPEED_HIGHTRH		11   // m/sec, speed LT/min. alt. threshold

~~~

#define PM_DISTTO_HOME		160  // m min distance threshold to trigger auto RTH and land

#define PM_CKMAX_FLIGHTDIST           1000 // m max distance perimeter threshold to auto trigger RTH and land

#define PM_LANDRTGL_REPEATS	   2   // number of semi-rounded rectangles before landing

const struct logoInstructionDef instructions[] = {

~~~

//  ****************  COMMON PROGRAMS  ****************

~~~

IF_LT(LOGO_B_CHANNEL,PM_TXKNOB_SECQTL)  	//do wider circles PARAM x and then AUTOLAND

IF_GE(ALT_SONAR, 0)

IF_LT(ALT_SONAR,PM_TKOFF_SNRALT)  // if less than 300cm do autotakeoff

DO_ARG(CM_CC_AUTOTAKEOFF,PM_LONG_RTGLLEG)

END

ELSE

IF_LT(ALT,PM_TKOFF_GPSALT) 		// if less than 3m do autotakeoff

DO_ARG(CM_CC_AUTOTAKEOFF,PM_LONG_RTGLLEG)

END

END

REPEAT(PM_LANDRTGL_REPEATS)		// do landing rect. 2x

DO_ARG(CM_CC_RECTANGLE,PM_LONG_RTGLLEG)

END

DO_ARG(CM_AUTOLAND,PM_LANDG_SPAN)	// do auto land

ELSE

~~~

//  ****************  AUTONOMOUS SOFT LANDING PROGRAM  ****************

TO (CM_AUTOLAND)				// Landing approach

PEN_UP				// ALIGN LANDING WITH PATTERN'S LAST LEG

USE_CURRENT_POS    		// aim for the current flightplan x,y position target

USE_ANGLE_TO_GOAL  		// aim for the current flightplan angle target

BK_PARAM 	   		// defines total landing distance from goal

PARAM_DIV(10)

FLAG_ON(F_LAND)    		// TURN OFF THROTTLE TO start powerless landing glide

SET_ALT_PARAM		// At 200 param, this is eq. to 20 m alt

PARAM_MUL(2)

FD_PARAM			// At 200 param, this is eq. to 40 m

PARAM_DIV(4)

SET_ALT_PARAM		// At 200 param, this is eq. to 10 m alt

PARAM_MUL(4)

FD_PARAM			// At 200 param, this is eq. to 40 m

PEN_DOWN

IF_GE(ALT_SONAR, 0)		// Chk for a sonar attached, if none, dummy would be -1

IF_LT(ALT_SONAR,PM_LANDG_APRCH_SNRALT) // check altitude using sonar data						FLAG_OFF(F_LAND) 	// throttle up for flare to moderate descend

SET_ALT(PM_LANDG_APRCH_GPSALT) // At 200 param, this is eq. to 3 m alt

FD(PM_LANDG_APCHSEG_FD)	// ADD flare dist. (FD)

FLAG_ON(F_LAND) 	// Throttle off and continue powerless landing trajectory

ELSE

SET_ALT(PM_LANDG_APRCH_GPSALT)  // At 200 param, this is eq. to 3 m alt

END

ELSE

IF_LT(ALT,PM_LANDG_APRCH_GPSALT)  // Use ALT if no sonar is attached

FLAG_OFF(F_LAND)

SET_ALT(PM_LANDG_APRCH_GPSALT)  // At 200 param, this is eq. to 3 m alt

FD(PM_LANDG_APCHSEG_FD)	// ADD flare dist. (FD)

FLAG_ON(F_LAND) 	// Throttle off and continue powerless glide

END

END

FD_PARAM				// At 200 m param, eq. to 40 m, AT THIS POINT,  120m distance

PARAM_MUL(2)			// define 80 meters landing span PARAM for CM_LAND_SONAR

DO_PARAM(CM_LAND_SONAR)

END

TO (CM_LAND_SONAR)				// Manage soft landing

PEN_UP

USE_CURRENT_POS    		// aim for the current flightplan x,y position target

USE_ANGLE_TO_GOAL  		// aim for the current flightplan angle target

BK_PARAM 			// At 200 m param, 80 meters landing span from goal

PARAM_DIV(4)			// FOUR landing segments, each with 20m span at 200 PARAM

IF_GE(ALT_SONAR, 0)		// FST (first) landing segment

IF_LT(ALT_SONAR,PM_LANDG_FSTSEG_SNRALT)// check sonar alt. if less than 2.8 m

FLAG_OFF(F_LAND) 	// throttle up, flare and

SET_ALT(PM_LANDG_FSTSEG_GPSALT) // moderately level the descend

FD(PM_LANDG_FSTSEG_FD)  // forward dist.

FLAG_ON(F_LAND) 	// Throttle off and continue powerless glide

ELSE

SET_ALT(PM_LANDG_FSTSEG_GPSALT)

END

ELSE

SET_ALT(PM_LANDG_FSTSEG_GPSALT)

END

FD_PARAM

PEN_DOWN

IF_GE(ALT_SONAR, 0)			// SEC (second) landing segment

IF_LT(ALT_SONAR,PM_LANDG_SECSEG_SNRALT)

FLAG_OFF(F_LAND)

SET_ALT(PM_LANDG_SECSEG_GPSALT)

FD(PM_LANDG_SECSEG_FD)

FLAG_ON(F_LAND)

ELSE

SET_ALT(PM_LANDG_SECSEG_GPSALT)

END

ELSE

SET_ALT(PM_LANDG_SECSEG_GPSALT)

END				// If not true, skip this segment, continue landing trajectory

FD_PARAM

IF_GE(ALT_SONAR, 0)		//  TRD (third) landing segment

IF_LT(ALT_SONAR,PM_LANDG_TRDSEG_SNRALT)

FLAG_OFF(F_LAND)

SET_ALT(PM_LANDG_TRDSEG_GPSALT)

FD(PM_LANDG_TRDSEG_FD)

FLAG_ON(F_LAND)

ELSE

SET_ALT(PM_LANDG_TRDSEG_GPSALT)

END

ELSE

SET_ALT(PM_LANDG_TRDSEG_GPSALT)

END

FD_PARAM

FLAG_ON(F_LAND) 		//  FTH (fourth) segment level pitch descend till touch down

FD_PARAM

END

~~~