| MCQS of CS401 |
| --- |
| ( ) |
| Attention: Material on Vugujranwala.com is Legally Copyrighted under Pakistan Law. Publishing it in any way is illegal and will be a Police Case. |
| Question # 1 |
|  | There are three busses to communicate the processor and memory named as _____________ |
|  | 1) : | address bus.,data bus and data bus. |
|  | 2) : | addressing bus.,data bus and data bus. |
|  | 3) : | address bus.,datamove bus and data bus. |
|  | 4) : | address bus.,data bus and control bus.. |
|  | Correct Option : 4 | From : | Lecture 1 |
| . |
| Question # 2 |
|  | The address bus is unidirectional and address always travels from processor to memory. |
|  | 1) : | TRUE |
|  | 2) : | FALSE |
|  | 3) : |  |
|  | 4) : |  |
|  | Correct Option : 1 | From : | Lecture 1 |
| . |
| Question # 3 |
|  | Data bus is bidirectional because________ |
|  | 1) : | To way |
|  | 2) : | Data moves from both, processor to memory and memory to processor, |
|  | 3) : | Data moves from both, processor to memory and memory to data Bus, |
|  | 4) : | None of the Given |
|  | Correct Option : 3 | From : | Lecture 1 |
| . |
| Question # 4 |
|  | Control bus________ |
|  | 1) : | is Not Important |
|  | 2) : | is Important |
|  | 3) : | bidirectional |
|  | 4) : | unidirectional |
|  | Correct Option : 3 | From : | Lecture 1 |
| . |
| Question # 5 |
|  | A memory cell is an n-bit location to store data, normally ________also called a byte |
|  | 1) : | 4-bit |
|  | 2) : | 8-bit |
|  | 3) : | 6-bit |
|  | 4) : | 80-bit |
|  | Correct Option : 2 | From : | Lecture 1 |
| . |
| Question # 6 |
|  | The number of bits in a cell is called the cell width.______________ define the memory completely. |
|  | 1) : | Cell width and number of cells, |
|  | 2) : | cell number and width of the cells, |
|  | 3) : | width |
|  | 4) : | Height |
|  | Correct Option : 1 | From : | Lecture 1 |
| . |
| Question # 7 |
|  | for memory we define two dimensions. The first dimension defines how many __________bits are there in a single memory cell. |
|  | 1) : | parallel |
|  | 2) : | Vertical |
|  | 3) : | long |
|  | 4) : | short |
|  | Correct Option : 1 | From : | Lecture 1 |
| . |
| Question # 8 |
|  | __________ operation requires the same size of data bus and memory cell width. |
|  | 1) : | Normal |
|  | 2) : | Best and simplest |
|  | 3) : | first |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 1 |
| . |
| Question # 9 |
|  | Control bus is only the mechanism. The responsibility of sending the appropriate signals on the control bus to the memory is of the_________________. |
|  | 1) : | Data Bus |
|  | 2) : | processor |
|  | 3) : | Address Bus |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 1 |
| . |
| Question # 10 |
|  | In “total: dw 0 ” Opcode total is a ___________ |
|  | 1) : | Literal |
|  | 2) : | Variable |
|  | 3) : | Label |
|  | 4) : | Starting point |
|  | Correct Option : 3 | From : | Lecture 10 |
| . |
| Question # 11 |
|  | ¦ 0 ¦--›¦ 1 ¦ 1 ¦ 0 ¦ 1 ¦ 0 ¦ 0 ¦ 0 ¦ --›¦ C ¦ is a example of ______ |
|  | 1) : | Shl |
|  | 2) : | sar |
|  | 3) : | Shr |
|  | 4) : | Sal |
|  | Correct Option : 3 | From : | Lecture 10 |
| . |
| Question # 12 |
|  | ¦ C ¦‹--¦ 1 ¦ 1 ¦ 0 ¦ 1 ¦ 0 ¦ 0 ¦ 0 ¦ ‹--¦ 0 ¦ is a example of ______ |
|  | 1) : | Shl |
|  | 2) : | sar |
|  | 3) : | Shr |
|  | 4) : | Sal |
|  | Correct Option : 1 | From : | Lecture 10 |
| . |
| Question # 13 |
|  | ADC has _________ operands. |
|  | 1) : | two |
|  | 2) : | three |
|  | 3) : | Five |
|  | 4) : | Zero |
|  | Correct Option : 2 | From : | Lecture 10 |
| . |
| Question # 14 |
|  | The basic purpose of a computer is to perform operations, and operations need ____________. |
|  | 1) : | order |
|  | 2) : | nothing |
|  | 3) : | operands |
|  | 4) : | bit |
|  | Correct Option : 3 | From : | Lecture 2 |
| . |
| Question # 15 |
|  | Registers are like a scratch pad ram inside the processor and their operation is very much like normal______________. |
|  | 1) : | Number |
|  | 2) : | opreations |
|  | 3) : | memory cells |
|  | 4) : | None of the Given |
|  | Correct Option : 3 | From : | Lecture 2 |
| . |
| Question # 16 |
|  | There is a central register in every processor called the _______ and The word size of a processor is defined by the width of its__________. |
|  | 1) : | accumulator,accumulator |
|  | 2) : | data bus,accumulator |
|  | 3) : | accumulator, Address Bus |
|  | 4) : | accumulator, memory |
|  | Correct Option : 1 | From : | Lecture 2 |
| . |
| Question # 17 |
|  | ___________does not hold data but holds the address of data |
|  | 1) : | Pointer, Segment, or Base Register |
|  | 2) : | Pointer, Index, or Base Register |
|  | 3) : | General Registers |
|  | 4) : | Instruction Pointer |
|  | Correct Option : 2 | From : | Lecture 2 |
| . |
| Question # 18 |
|  | “The program counter holds the address of the next instruction to be _____________” |
|  | 1) : | executed |
|  | 2) : | called |
|  | 3) : | deleted |
|  | 4) : | copy |
|  | Correct Option : 1 | From : | Lecture 2 |
| . |
| Question # 19 |
|  | There are _____ types of “instruction groups” |
|  | 1) : | 4 |
|  | 2) : | 5 |
|  | 3) : | 3 |
|  | 4) : | 2 |
|  | Correct Option : 1 | From : | Lecture 2 |
| . |
| Question # 20 |
|  | These instructions are used to move data from one place to another. |
|  | 1) : | TRUE |
|  | 2) : | FALSE |
|  | 3) : |  |
|  | 4) : |  |
|  | Correct Option : 1 | From : | Lecture 2 |
| . |
| Question # 21 |
|  | “mov” instruction is related to the _______ Group. |
|  | 1) : | Arithmetic and Logic Instructions |
|  | 2) : | Data Movement Instructions |
|  | 3) : | Program Control Instructions |
|  | 4) : | Special Instructions |
|  | Correct Option : 2 | From : | Lecture 2 |
| . |
| Question # 22 |
|  | ______________allow changing specific processor behaviors and are used to play with it. |
|  | 1) : | Special Instructions |
|  | 2) : | Data Movement Instructions |
|  | 3) : | Program Control Instructions |
|  | 4) : | Arithmetic and Logic Instructions |
|  | Correct Option : 1 | From : | Lecture 2 |
| . |
| Question # 23 |
|  | 8088 is a 16bit processor with its accumulator and all registers of __________. |
|  | 1) : | 32 bits |
|  | 2) : | 6 bits |
|  | 3) : | 16 bits |
|  | 4) : | 64 bits |
|  | Correct Option : 3 | From : | Lecture 2 |
| . |
| Question # 24 |
|  | The __________ of a processor means the organization and functionalities of the registers it contains and the instructions that are valid on the processor. |
|  | 1) : | Manufactures |
|  | 2) : | architecture |
|  | 3) : | Deal |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 2 |
| . |
| Question # 25 |
|  | Intel IAPX88 Architecture is ___________ |
|  | 1) : | More than 25 old |
|  | 2) : | New |
|  | 3) : | Not Good |
|  | 4) : | None of the Given |
|  | Correct Option : 1 | From : | Lecture 2 |
| . |
| Question # 26 |
|  | The iAPX88 architecture consists of______registers. |
|  | 1) : | 13 |
|  | 2) : | 12 |
|  | 3) : | 9 |
|  | 4) : | 14 |
|  | Correct Option : 4 | From : | Lecture 3 |
| . |
| Question # 27 |
|  | General Registers are ______________ |
|  | 1) : | AX, BX, CX, and DX |
|  | 2) : | XA, BX, CX, and DX |
|  | 3) : | SS,SI and DI |
|  | 4) : | 3 |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 28 |
|  | AX means we are referring to the extended 16bit “A” register. Its upper and lower byte are separately accessible as ________________. |
|  | 1) : | AH and AL |
|  | 2) : | A Lower and A Upper |
|  | 3) : | AL, AU |
|  | 4) : | AX |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 29 |
|  | AX is General purpose Register where A stands for__________. |
|  | 1) : | Acadmic |
|  | 2) : | Ado |
|  | 3) : | Architecture |
|  | 4) : | Accumulator |
|  | Correct Option : 4 | From : | Lecture 3 |
| . |
| Question # 30 |
|  | The B of BX stands for _________because of its role in memory addressing. |
|  | 1) : | Busy |
|  | 2) : | Base |
|  | 3) : | Better |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 3 |
| . |
| Question # 31 |
|  | The D of DX stands for Destination as it acts as the destination in _____________________. |
|  | 1) : | I/O operations |
|  | 2) : | operations |
|  | 3) : | memory cells |
|  | 4) : | Memory I/O operations |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 32 |
|  | The C of CX stands for Counter as there are certain instructions that work with an automatic count in the ___________. |
|  | 1) : | DI register |
|  | 2) : | BX register |
|  | 3) : | CX register |
|  | 4) : | DX register |
|  | Correct Option : 3 | From : | Lecture 3 |
| . |
| Question # 33 |
|  | _________are the index registers of the Intel architecture which hold address of data and used in memory access. |
|  | 1) : | SI and SS |
|  | 2) : | PI and DI |
|  | 3) : | SI and IP |
|  | 4) : | SI and DI |
|  | Correct Option : 4 | From : | Lecture 3 |
| . |
| Question # 34 |
|  | In Intel IAPX88 architecture ___________ is the special register containing the address of the next instruction to be executed. |
|  | 1) : | AX |
|  | 2) : | PI |
|  | 3) : | IP |
|  | 4) : | SI |
|  | Correct Option : 3 | From : | Lecture 3 |
| . |
| Question # 35 |
|  | SP is a memory pointer and is used indirectly by a set of ____________. |
|  | 1) : | instructions |
|  | 2) : | Pointers |
|  | 3) : | Indexes |
|  | 4) : | Variables |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 36 |
|  | ___________is also a memory pointer containing the address in a special area of memory called the stack. |
|  | 1) : | SP |
|  | 2) : | BP |
|  | 3) : | PB |
|  | 4) : | AC |
|  | Correct Option : 2 | From : | Lecture 3 |
| . |
| Question # 37 |
|  | ____________is bit wise significant and accordingly each bit is named separately. |
|  | 1) : | AX |
|  | 2) : | FS |
|  | 3) : | IP |
|  | 4) : | Flags Register |
|  | Correct Option : 4 | From : | Lecture 3 |
| . |
| Question # 38 |
|  | When two 16bit numbers are added the answer can be 17 bits long, this extra bit that won’t fit in the target register is placed in the __________where it can be used and tested |
|  | 1) : | carry flag |
|  | 2) : | Parity Flag |
|  | 3) : | Auxiliary Carry |
|  | 4) : | Zero Flag |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 39 |
|  | Program is an ordered set of instructions for the processor. |
|  | 1) : | TRUE |
|  | 2) : | FALSE |
|  | 3) : |  |
|  | 4) : |  |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 40 |
|  | For Intel Architecture “operation destination, source” is way of writing things. |
|  | 1) : | TRUE |
|  | 2) : | FALSE |
|  | 3) : |  |
|  | 4) : |  |
|  | Correct Option : 1 | From : | Lecture 3 |
| . |
| Question # 41 |
|  | Operation code “ add ax, bx ” ____________. |
|  | 1) : | Add the bx to ax and change the bx |
|  | 2) : | Add the ax to bx and change the ax |
|  | 3) : | Add the bx to ax and change the ax |
|  | 4) : | Add the bx to ax and change nothing |
|  | Correct Option : 3 | From : | Lecture 3 |
| . |
| Question # 42 |
|  | The maximum memory iAPX88 can access is________________. |
|  | 1) : | 1MB |
|  | 2) : | 2MB |
|  | 3) : | 3MB |
|  | 4) : | 128MB |
|  | Correct Option : 1 | From : | Lecture 4 |
| . |
| Question # 43 |
|  | The maximum memory iAPX88 can access is 1MB which can be accessed with _______________. |
|  | 1) : | 18 bits |
|  | 2) : | 20 bits |
|  | 3) : | 16 bits |
|  | 4) : | 2 bits |
|  | Correct Option : 2 | From : | Lecture 4 |
| . |
| Question # 44 |
|  | _____________address of 1DED0 where the opcode B80500 is placed. |
|  | 1) : | physical memory |
|  | 2) : | memory |
|  | 3) : | efective |
|  | 4) : | None of the Given |
|  | Correct Option : 1 | From : | Lecture 4 |
| . |
| Question # 45 |
|  | 16 bit of Segment and Offset Addresses can be converted to 20bit Address i.e Segment Address with lower four bits zero + Offset Address with ______ four bits zero = 20bit Physical Address |
|  | 1) : | Middle |
|  | 2) : | lower |
|  | 3) : | Top |
|  | 4) : | upper |
|  | Correct Option : 4 | From : | Lecture 4 |
| . |
| Question # 46 |
|  | When adding two 20bit Addresses a carry if generated is dropped without being stored anywhere and the phenomenon is called address______. |
|  | 1) : | wraparound |
|  | 2) : | mode |
|  | 3) : | ping |
|  | 4) : | error |
|  | Correct Option : 1 | From : | Lecture 4 |
| . |
| Question # 47 |
|  | Segments can only be defined a 16byte boundaries called _____________ boundaries. |
|  | 1) : | segment |
|  | 2) : | paragraph |
|  | 3) : | Cell |
|  | 4) : | RAM |
|  | Correct Option : 1 | From : | Lecture 4 |
| . |
| Question # 48 |
|  | in a Program CS, DS, SS, and ES all had the same value in them. This is called _____________________. |
|  | 1) : | equel memory |
|  | 2) : | overlapping segments |
|  | 3) : | segments hidding |
|  | 4) : | overlapping SI |
|  | Correct Option : 2 | From : | Lecture 4 |
| . |
| Question # 49 |
|  | “db num1” size of the memory is _____________ |
|  | 1) : | 1byte |
|  | 2) : | 4bit |
|  | 3) : | 16bit |
|  | 4) : | 2byte |
|  | Correct Option : 1 | From : | Lecture 5 |
| . |
| Question # 50 |
|  | “ 1------------[org 0x0100] 2------------mov ax, [num1] ; load first number in ax 3------------mov bx, [num2] ; load second number in bx 4------------add ax, bx _________________________________ 5------------int 0x21 6------------ 7------------num1: dw 5 8------------num2: dw 10 Comments for the 4 are : |
|  | 1) : | No comments Will be |
|  | 2) : | ; accumulate sum in add |
|  | 3) : | ; accumulate sum in ax |
|  | 4) : | ; accumulate sum in Bx |
|  | Correct Option : 3 | From : | Lecture 5 |
| . |
| Question # 51 |
|  | In “ mov ax, bx ” is _____________ Addressing Modes. |
|  | 1) : | Immediate |
|  | 2) : | Indirect |
|  | 3) : | Direct |
|  | 4) : | Register |
|  | Correct Option : 4 | From : | Lecture 5 |
| . |
| Question # 52 |
|  | In “mov ax, [bx] ” is _____________ Addressing Modes |
|  | 1) : | Based Register Indirect |
|  | 2) : | Indirect |
|  | 3) : | Base Indirect |
|  | 4) : | Immediate |
|  | Correct Option : 1 | From : | Lecture 5 |
| . |
| Question # 53 |
|  | In “mov ax, 5 ” is _____________ Addressing Modes |
|  | 1) : | Immediate |
|  | 2) : | Indirect |
|  | 3) : | Indirect |
|  | 4) : | Register |
|  | Correct Option : 1 | From : | Lecture 6 |
| . |
| Question # 54 |
|  | In “ mov ax, [num1+bx] ” is ___________ ADDRESSING |
|  | 1) : | OFFSET+ Indirect |
|  | 2) : | Register + Direct |
|  | 3) : | Indirect + Reference |
|  | 4) : | BASEd REGISTER + OFFSET |
|  | Correct Option : 4 | From : | Lecture 7 |
| . |
| Question # 55 |
|  | “base + offset addressing ” gives This number which came as the result of addition is called the _______. |
|  | 1) : | Address |
|  | 2) : | mode |
|  | 3) : | effective address |
|  | 4) : | Physical Address |
|  | Correct Option : 3 | From : | Lecture 7 |
| . |
| Question # 56 |
|  | “mov ax, [cs:bx]” associates _________ for this one instruction |
|  | 1) : | CS with BX |
|  | 2) : | BX with CS |
|  | 3) : | BX with AX |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 7 |
| . |
| Question # 57 |
|  | For example BX=0100 DS=FFF0 And Opcode are; move [bx+0x0100], Ax now what is the effective memory address; |
|  | 1) : | 0020 |
|  | 2) : | 0200 |
|  | 3) : | 0300 |
|  | 4) : | 0x02 |
|  | Correct Option : 2 | From : | Lecture 7 |
| . |
| Question # 58 |
|  | For example BX=0100 DS=FFF0 And Opcode are; move [bx+0x0100], Ax now what is the physical memory address; |
|  | 1) : | 0020 |
|  | 2) : | 0x0100 |
|  | 3) : | 0x10100 |
|  | 4) : | 0x100100 |
|  | Correct Option : 2 | From : | Lecture 7 |
| . |
| Question # 59 |
|  | In “ mov [1234], al ” is _____________ Addressing Modes. |
|  | 1) : | Immediate |
|  | 2) : | Indirect |
|  | 3) : | Direct |
|  | 4) : | Register |
|  | Correct Option : 3 | From : | Lecture 8 |
| . |
| Question # 60 |
|  | In “ mov [SI], AX ” is _____________ Addressing Modes. |
|  | 1) : | Basef Register Indirect |
|  | 2) : | Indirect |
|  | 3) : | Indexed Register Indirect |
|  | 4) : | Immediate |
|  | Correct Option : 3 | From : | Lecture 8 |
| . |
| Question # 61 |
|  | In “ mov ax, [bx - Si] ” is ___________ ADDRESSING |
|  | 1) : | Basef Register Indirect |
|  | 2) : | Indirect |
|  | 3) : | Direct |
|  | 4) : | illegal |
|  | Correct Option : 4 | From : | Lecture 8 |
| . |
| Question # 62 |
|  | In “ mov ax, [BL] ” there is error i.e. __________ |
|  | 1) : | Address must be 16bit |
|  | 2) : | Address must be 8bit |
|  | 3) : | Address must be 4bit |
|  | 4) : | 8 bit to 16 bit move illegal |
|  | Correct Option : 4 | From : | Lecture 8 |
| . |
| Question # 63 |
|  | In “ mov ax, [SI+DI] ” there is error i.e. __________ |
|  | 1) : | Two indexes can’t use as Memory Address |
|  | 2) : | index can’t use as Memory Address |
|  | 3) : | I don't Know |
|  | 4) : | None of the Given |
|  | Correct Option : 1 | From : | Lecture 8 |
| . |
| Question # 64 |
|  | In JNE and JNZ there is difference for only _____________; |
|  | 1) : | Programmer or Logic |
|  | 2) : | Assembler |
|  | 3) : | Debugger |
|  | 4) : | IAPX88 |
|  | Correct Option : 1 | From : | Lecture 9 |
| . |
| Question # 65 |
|  | JMP is Instruction that on executing take jump regardless of the state of all flags is called__________ |
|  | 1) : | Jump |
|  | 2) : | Conditional jump |
|  | 3) : | Unconditional jump |
|  | 4) : | Stay |
|  | Correct Option : 3 | From : | Lecture 9 |
| . |
| Question # 66 |
|  | When result of the source subtraction from the destination is zero, zero flag is set i.e. ZF=1 its mean that; |
|  | 1) : | DEST = SRC |
|  | 2) : | DEST != SRC |
|  | 3) : | DEST < SRC |
|  | 4) : | DEST > SRC |
|  | Correct Option : 1 | From : | Lecture 9 |
| . |
| Question # 67 |
|  | When an unsigned source is subtracted from an unsigned destination and the destination is smaller, borrow is needed which sets the ____________. |
|  | 1) : | carry flag i.e CF = 0 |
|  | 2) : | carry flag i.e CF = 1 |
|  | 3) : | Carry Flag + ZF=1 |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 9 |
| . |
| Question # 68 |
|  | In the case of unassigned source and destination when subtracting and in the result ZF =1 OR CR=1 then _______ |
|  | 1) : | DEST = SRC |
|  | 2) : | DEST != SRC |
|  | 3) : | UDEST ? USRC |
|  | 4) : | DEST > SRC |
|  | Correct Option : 3 | From : | Lecture 9 |
| . |
| Question # 69 |
|  | In the case of unassigned source and destination when subtracting and in the result ZF =0 AND CR=0 then _______ |
|  | 1) : | DEST = SRC |
|  | 2) : | DEST != SRC |
|  | 3) : | UDEST < USRC |
|  | 4) : | UDEST > USRC |
|  | Correct Option : 4 | From : | Lecture 9 |
| . |
| Question # 70 |
|  | In the case of unassigned source and destination when subtracting and in the result CR=0 then _______ |
|  | 1) : | DEST = SRC |
|  | 2) : | DEST != SRC |
|  | 3) : | UDEST < USRC |
|  | 4) : | UDEST ? USRC |
|  | Correct Option : 4 | From : | Lecture 9 |
| . |
| Question # 71 |
|  | ______This jump is taken if the last arithmetic operation produced a zero in its destination. After a CMP it is taken if both operands were equal. |
|  | 1) : | Jump if zero(JZ)/Jump if equal(JE) |
|  | 2) : | Jump if equal(JE) |
|  | 3) : | Jump if zero(JZ) |
|  | 4) : | No Jump fot This |
|  | Correct Option : 1 | From : | Lecture 9 |
| . |
| Question # 72 |
|  | _______This jump is taken after a CMP if the unsigned source is smaller than or equal to the unsigned destination. |
|  | 1) : | JBE(Jump if not below or equal) |
|  | 2) : | JNA(Jump if not above)/JBE(Jump if not below or equal) |
|  | 3) : | JNA(Jump if not above) |
|  | 4) : | No Jump fot This |
|  | Correct Option : 2 | From : | Lecture 9 |
| . |
| Material on Vugujranwala.com is Legally Copyrighted under Pakistan Law. Publishing it in any Form is illegal and will be a Police Case. |
| Copyright © VuGujranwala.com Powered By: Group of Virtual's Experts |
| MCQS of CS401 |
| ( ) |
| Attention: Material on Vugujranwala.com is Legally Copyrighted under Pakistan Law. Publishing it in any way is illegal and will be a Police Case. |
| Question # 1 |
|  | Numbers of any size can be added using a proper combination of __________. |
|  | 1) : | ADD and ADC |
|  | 2) : | ABD and ADC |
|  | 3) : | ADC and ADC |
|  | 4) : | None of the Given |
|  | Correct Option : 1 | From : | Lecture 11 |
| . |
| Question # 2 |
|  | Like addition with carry there is an instruction to subtract with borrows called____________. |
|  | 1) : | SwB |
|  | 2) : | SBB |
|  | 3) : | SBC |
|  | 4) : | SBBC |
|  | Correct Option : 2 | From : | Lecture 11 |
| . |
| Question # 3 |
|  | if “and ax, bx” instruction is given, There are _____________ operations as a result |
|  | 1) : | 16 AND |
|  | 2) : | 17 AND |
|  | 3) : | 32 AND |
|  | 4) : | 8 AND |
|  | Correct Option : 1 | From : | Lecture 12 |
| . |
| Question # 4 |
|  | ____________can be used to check whether particular bits of a number are set or not. |
|  | 1) : | AND |
|  | 2) : | OR |
|  | 3) : | XOR |
|  | 4) : | NOT |
|  | Correct Option : 1 | From : | Lecture 12 |
| . |
| Question # 5 |
|  | __________can also be used as a masking operation to invert selective bits. |
|  | 1) : | AND |
|  | 2) : | OR |
|  | 3) : | XOR |
|  | 4) : | NOT |
|  | Correct Option : 3 | From : | Lecture 12 |
| . |
| Question # 6 |
|  | Masking Operations are Selective Bit ______________________ |
|  | 1) : | Clearing, XOR, Inversion and Testing |
|  | 2) : | Clearing, Setting, Inversion and Testing |
|  | 3) : | Clearing, XOR, AND and Testing |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 12 |
| . |
| Question # 7 |
|  | The ____________ instruction allows temporary diversion and therefore reusability of code. |
|  | 1) : | CALL |
|  | 2) : | RET |
|  | 3) : | AND |
|  | 4) : | XOR |
|  | Correct Option : 1 | From : | Lecture 13 |
| . |
| Question # 8 |
|  | CALL takes a label as _____________ and execution starts from that label, |
|  | 1) : | argument |
|  | 2) : | Lable |
|  | 3) : | TXt |
|  | 4) : | Register |
|  | Correct Option : 1 | From : | Lecture 13 |
| . |
| Question # 9 |
|  | When the __________instruction is encountered and it takes execution back to the instruction following the CALL. |
|  | 1) : | CALL |
|  | 2) : | RET |
|  | 3) : | AND |
|  | 4) : | XOR |
|  | Correct Option : 2 | From : | Lecture 13 |
| . |
| Question # 10 |
|  | _______________________ Both the instructions are commonly used as a pair, however technically they are independent in their operation. |
|  | 1) : | RET and ADC |
|  | 2) : | Cal and SSb |
|  | 3) : | CALL and RET |
|  | 4) : | ADC and SSB |
|  | Correct Option : 3 | From : | Lecture 13 |
| . |
| Question # 11 |
|  | The CALL mechanism breaks the thread of execution and does not change registers, except ____________. |
|  | 1) : | SI |
|  | 2) : | IP |
|  | 3) : | DI |
|  | 4) : | SP |
|  | Correct Option : 2 | From : | Lecture 13 |
| . |
| Question # 12 |
|  | Stack is a ______ that behaves in a first in last out manner. |
|  | 1) : | Program |
|  | 2) : | data structure |
|  | 3) : | Heap |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 14 |
| . |
| Question # 13 |
|  | If ____________ is not available, stack clearing by the callee is a complicated process. |
|  | 1) : | CALL |
|  | 2) : | SBB |
|  | 3) : | RET n |
|  | 4) : | None of the Given |
|  | Correct Option : 3 | From : | Lecture 14 |
| . |
| Question # 14 |
|  | When the stack will eventually become full, SP will reach 0, and thereafter wraparound producing unexpected results. This is called stack ________ |
|  | 1) : | Overflow |
|  | 2) : | Leakage |
|  | 3) : | Error |
|  | 4) : | Pointer |
|  | Correct Option : 1 | From : | Lecture 14 |
| . |
| Question # 15 |
|  | The pop operation makes a copy from the top of the stack into its_______________. |
|  | 1) : | Register |
|  | 2) : | operand |
|  | 3) : | RET n |
|  | 4) : | Pointer |
|  | Correct Option : 2 | From : | Lecture 14 |
| . |
| Question # 16 |
|  | _______________decrements SP (the stack pointer) by two and then transfers a word from the source operand to the top of stack |
|  | 1) : | PUSH |
|  | 2) : | POP |
|  | 3) : | CALL |
|  | 4) : | RET |
|  | Correct Option : 1 | From : | Lecture 14 |
| . |
| Question # 17 |
|  | POP transfers the word at the current top of stack (pointed to by SP) to the destination operand and then __________ SP by two to point to the new top of stack. |
|  | 1) : | increments |
|  | 2) : | dcrements |
|  | 3) : | ++ |
|  | 4) : | -- |
|  | Correct Option : 1 | From : | Lecture 14 |
| . |
| Question # 18 |
|  | The trick is to use the ________and ___________operations and save the callers’ value on the stack and recover it from there on return. |
|  | 1) : | POP, ADC |
|  | 2) : | CALL, RET |
|  | 3) : | CALL, RET n |
|  | 4) : | PUSH, POP |
|  | Correct Option : 4 | From : | Lecture 14 |
| . |
| Question # 19 |
|  | To access the arguments from the stack, the immediate idea that strikes is to __________ them off the stack. |
|  | 1) : | PUSH |
|  | 2) : | POP |
|  | 3) : | CALL |
|  | 4) : | Register |
|  | Correct Option : 2 | From : | Lecture 15 |
| . |
| Question # 20 |
|  | push bp we are ________________ |
|  | 1) : | sending bp copy to stack |
|  | 2) : | making bp copy from stack |
|  | 3) : | pushing bp on the stack |
|  | 4) : | doing nothing |
|  | Correct Option : 3 | From : | Lecture 15 |
| . |
| Question # 21 |
|  | Local Variables means variables that are used within the ___________________ |
|  | 1) : | Subroutine |
|  | 2) : | Program |
|  | 3) : | CALL |
|  | 4) : | Label |
|  | Correct Option : 1 | From : | Lecture 15 |
| . |
| Question # 22 |
|  | Standard ASCII has 128 characters with assigned numbers from ________. |
|  | 1) : | 1to 129 |
|  | 2) : | 0 to 127 |
|  | 3) : | 0 to 128 |
|  | 4) : | None of the Given |
|  | Correct Option : 2 | From : | Lecture 16 |
| . |
| Question # 23 |
|  | When _______ is sent to the VGA card, it will turn pixels on and off in such a way that a visual representation of ‘A’ appears on the screen. |
|  | 1) : | 0x60 |
|  | 2) : | 0x90 |
|  | 3) : | 0x30 |
|  | 4) : | 0x40 |
|  | Correct Option : 4 | From : | Lecture 16 |
| . |
| Question # 24 |
|  | Which bit is refer to the Blinking of foreground character |
|  | 1) : | 6 |
|  | 2) : | 7 |
|  | 3) : | 5 |
|  | 4) : | 3 |
|  | Correct Option : 2 | From : | Lecture 16 |
| . |
| Question # 25 |
|  | Which bit is refer to the Intensity component of foreground color |
|  | 1) : | 4 |
|  | 2) : | 5 |
|  | 3) : | 3 |
|  | 4) : | 7 |
|  | Correct Option : 3 | From : | Lecture 16 |
| . |
| Question # 26 |
|  | Which bit is refer to the Green component of background color |
|  | 1) : | 1 |
|  | 2) : | 5 |
|  | 3) : | 3 |
|  | 4) : | 7 |
|  | Correct Option : 2 | From : | Lecture 16 |
| . |
| Question # 27 |
|  | Which bit is refer to the Green component of foreground color |
|  | 1) : | 1 |
|  | 2) : | 5 |
|  | 3) : | 3 |
|  | 4) : | 7 |
|  | Correct Option : 1 | From : | Lecture 16 |
| . |
| Question # 28 |
|  | String can be indicate bye given |
|  | 1) : | db 0x61, 0x61, 0x63 |
|  | 2) : | db 'a', 'b', 'c' |
|  | 3) : | db 'abc' |
|  | 4) : | All of the above |
|  | Correct Option : 4 | From : | Lecture 16 |
| . |
| Question # 29 |
|  | The first form divides a 32bit number in DX:AX by its 16bit operand and stores the ___________ quotient in AX |
|  | 1) : | 16bit |
|  | 2) : | 17bit |
|  | 3) : | 32bit |
|  | 4) : | 64bit |
|  | Correct Option : 1 | From : | Lecture 17 |
| . |
| Question # 30 |
|  | The ___________ (division) used in the process is integer division and not floating point division. |
|  | 1) : | DIV instruction |
|  | 2) : | ADC instruction |
|  | 3) : | SSB instruction |
|  | 4) : | DIVI instruction |
|  | Correct Option : 1 | From : | Lecture 17 |
| . |
| Question # 31 |
|  | ______________(multiply) performs an unsigned multiplication of the source operand and the accumulator. |
|  | 1) : | Multi |
|  | 2) : | DIV |
|  | 3) : | MUL |
|  | 4) : | Move |
|  | Correct Option : 3 | From : | Lecture 18 |
| . |
| Question # 32 |
|  | The desired location on the screen can be calculated with the following formulae. |
|  | 1) : | location = ( hypos * 80 + SP ) * 3 |
|  | 2) : | location = ( hypos * 80 + slocation ) * 2 |
|  | 3) : | location = ( hypos * 80 + epos ) * 2 |
|  | 4) : | None of the Given |
|  | Correct Option : 3 | From : | Lecture 18 |
| . |
| Question # 33 |
|  | To play with string there are 5 instructions that are __________ |
|  | 1) : | STOS, LODS, CMPS, SCAS, and MOVS |
|  | 2) : | MUL, DIV, ADD, ADC and MOVE |
|  | 3) : | SSB, ADD, CMPS, ADC, and MOVS |
|  | 4) : | None of the Given |
|  | Correct Option : 1 | From : | Lecture 18 |
| . |
| Question # 34 |
|  | _______transfers a byte or word from register AL or AX to the string element addressed by ES:DI and updates DI to point to the next location. |
|  | 1) : | LODS |
|  | 2) : | STOS |
|  | 3) : | SCAS |
|  | 4) : | MOVE |
|  | Correct Option : 2 | From : | Lecture 18 |
| . |
| Question # 35 |
|  | ____________ transfers a byte or word from the source location DS:SI to AL or AX and updates SI to point to the next location. |
|  | 1) : | LODS |
|  | 2) : | STOS |
|  | 3) : | SCAS |
|  | 4) : | MOVE |
|  | Correct Option : 1 | From : | Lecture 18 |
| . |
| Question # 36 |
|  | _______compares a source byte or word in register AL or AX with the destination string element addressed by ES: DI and updates the flags. |
|  | 1) : | LODS |
|  | 2) : | STOS |
|  | 3) : | SCAS |
|  | 4) : | MOVE |
|  | Correct Option : 3 | From : | Lecture 18 |
| . |
| Question # 37 |
|  | ____________ repeat the following string instruction while the zero flag is set and REPNE or REPNZ repeat the following instruction while the zero flag is not set. |
|  | 1) : | REP or REPZ |
|  | 2) : | REPE or REPZ |
|  | 3) : | REPE or RPZ |
|  | 4) : | RPE or REPZ |
|  | Correct Option : 2 | From : | Lecture 18 |
| . |
| Question # 38 |
|  | LES loads ______________ |
|  | 1) : | ES |
|  | 2) : | DS |
|  | 3) : | PS |
|  | 4) : | LS |
|  | Correct Option : 1 | From : | Lecture 20 |
| . |
| Question # 39 |
|  | LDS loads_______. |
|  | 1) : | ES |
|  | 2) : | DS |
|  | 3) : | PS |
|  | 4) : | LS |
|  | Correct Option : 2 | From : | Lecture 20 |
| . |
| Question # 40 |
|  | REP allows the instruction to be repeated ____________ times allowing blocks of memory to be copied. |
|  | 1) : | DX |
|  | 2) : | CX |
|  | 3) : | BX |
|  | 4) : | AX |
|  | Correct Option : 2 | From : | Lecture 20 |
| . |
| Question # 41 |
|  | ___________pops IP, then CS, and then FLAGS. |
|  | 1) : | Ret n |
|  | 2) : | REZA |
|  | 3) : | REPE |
|  | 4) : | IRET |
|  | Correct Option : 4 | From : | Lecture 21 |
| . |
| Question # 42 |
|  | ________ , Trap, Single step Interrupt |
|  | 1) : | INT 0 |
|  | 2) : | INT 1 |
|  | 3) : | INT 3 |
|  | 4) : | INT 0 |
|  | Correct Option : 2 | From : | Lecture 21 |
| . |
| Question # 43 |
|  | _________,NMI-Non Maskable Interrupt |
|  | 1) : | INT 0 |
|  | 2) : | INT 1 |
|  | 3) : | INT 3 |
|  | 4) : | INT 0 |
|  | Correct Option : 3 | From : | Lecture 21 |
| . |
| Question # 44 |
|  | To hook an interrupt we change the _________ corresponding to that interrupt. |
|  | 1) : | SX |
|  | 2) : | vector |
|  | 3) : | AX |
|  | 4) : | BX |
|  | Correct Option : 2 | From : | Lecture 22 |
| . |
| Material on Vugujranwala.com is Legally Copyrighted under Pakistan Law. Publishing it in any Form is illegal and will be a Police Case. |
| Copyright © VuGujranwala.com Powered By: Group of Virtual's Experts |
| MCQS of CS401 |
| ( ) |
| Attention: Material on Vugujranwala.com is Legally Copyrighted under Pakistan Law. Publishing it in any way is illegal and will be a Police Case. |
| Question # 1 |
|  | ___________pops IP, then CS, and then FLAGS. |
|  | 1) : | Ret n |
|  | 2) : | REZA |
|  | 3) : | REPE |
|  | 4) : | IRET |
|  | Correct Option : 4 | From : | Lecture 21 |
| . |
| Question # 2 |
|  | ________ , Trap, Single step Interrupt |
|  | 1) : | INT 0 |
|  | 2) : | INT 1 |
|  | 3) : | INT 3 |
|  | 4) : | INT 0 |
|  | Correct Option : 2 | From : | Lecture 21 |
| . |
| Question # 3 |
|  | _________,NMI-Non Maskable Interrupt |
|  | 1) : | INT 0 |
|  | 2) : | INT 1 |
|  | 3) : | INT 3 |
|  | 4) : | INT 0 |
|  | Correct Option : 3 | From : | Lecture 21 |
| . |
| Question # 4 |
|  | To hook an interrupt we change the _________ corresponding to that interrupt. |
|  | 1) : | SX |
|  | 2) : | vector |
|  | 3) : | AX |
|  | 4) : | BX |
|  | Correct Option : 2 | From : | Lecture 22 |
| . |
| Material on Vugujranwala.com is Legally Copyrighted under Pakistan Law. Publishing it in any Form is illegal and will be a Police Case. |
| Copyright © VuGujranwala.com Powered By: Group of Virtual's Experts |