## Slide 1: Outline specification for TREECYCLE electrical system
MGT Engineering Ltd

## Slide 2: Introduction
The TREECYCLE is produced in a number of versions, both electrically assisted and human powered only.
The basic electrical system is common to all models, having its own generator and battery back-up.
This allows the TREECYCLE to comply with German standards, which require the lighting system of an electrically assisted bicycle to be separate from the electrical assistance system, so ensuring that for safety reasons the supply to the lights is always guaranteed, even if for some reason power is not available from the large traction battery.
The system specification also allows for the use of standard lights, where these are required, also to meet different local standards in the markets where the TREECYCLE may be sold.

## Slide 3: Schematic system diagram
Handlebar switch cluster left/right Indicator switch horn button front/rear lights switch
Brake switches
2 into one from Tektro levers
Headlights
Brake lights
Rear light
Rear light
Indicators right
Indicators left
Display, docking station for location enabled cellphone, switch for hazard warning (all indicators together), general on/off ( key switch), LEDs for indicator function (2 yellow), lights on (1 blue) brake lights on (1 red)
Rotation sensor for
Distance and speed calculation
Central control box with back-up battery pack, external power supply connections for charging and optional input from traction battery
Left rear wheel shaft mounted 3 phase generator Sunup DS1-F with rectified output 3-12volts depending on wheel rotation speed

## Slide 4: Electrical specification
 | 3-50 volts DC
Main input from generator ( wheel rotation speed varies from 40-240 r.p.m, equivalent to 5- 30km/hour) | 3-12 volts DC
Optional input from electrical assistance battery | 36-50 volts DC
Optional input from photovoltaic cells | 6-50 volts DC
Battery back-up duration for lights in worst case (no traction battery or generator input, head, rear and four indicator lights all operating, all displays functional, discharged cell-phone connected) | 8 hours
Stored data memory duration ( trip/ total mileage any settings data) | 1 year
Output for cell-phone via USB, mini USB and micro USB ports | 5 volts DC
Output for standard commercial lights | 6 volts DC
Signal input for speed/distance travelled calculation/display | Supplier to confirm

## Slide 5: Functional requirements/characteristics
Commercially available front and rear lamps to european standards front: - Lumotec Lyt 25 lux x2, rear: - toplight mini x 2 http://www.bumm.de or equivalent.
Waterproof LED lamp units to IP65 for brake and indicator lights
Generator Sunup DS1-F http://www.sunupeco.com/SunUpEco/Products.html, or equivalent
Enclosures to be waterproof to IP65
Connections to be made between enclosures via waterproof plug/sockets
Non-standard lights may be on sealed/moulded harness as a single complete set
Speed/distance travelled display to be visible day and night